| Review of the City of Bothell Water System Plan, February 2011 |
| --- |
| Service Area The City of Bothell (the City) owns and operates a municipal water system that primarily serves the King County portion of the incorporated City as well as unincorporated lands in King County. The City’s retail service area is significantly smaller than the City limits and its urban growth area. The retail service area boundary serves a majority of the population located in the King County (south Bothell) portion of the City, and a small portion of population located in the Snohomish County (north Bothell) portion of the City. The remaining City population is served by the Northshore Utility District (NUD) in South Bothell and the Alderwood Water and Wastewater District (AWWD) in North Bothell, with a very small portion served by the Woodinville Water District (WWD). The City has no wholesale customers, no wholesale service area and its retail service area is not expected to change significantly in the foreseeable future. Encompassing 3,060 acres, the City’s proprietary water system includes three reservoirs, four booster stations and almost 75 miles of pipe. Its Franchise No. 7244 for water service expires July 5, 2013. Water Use Efficiency The City currently provides water service for approximately 17,000 people with 6,902 dwelling units for King County only; total City population served is 33,240 and 13,585 dwelling units. The number of equivalent residential units is 8,570. The City hosts approximately 11,550 employees on an average day. All of the City’s water is purchased from Seattle Public Utilities either directly, or wheeled through Northshore Utility District. The City has emergency interties with the AWWD, WWD and NUD. Average Daily Production 2003-2009 was 1.6 million gallons of water per day (mgd) and 3.04 mgd during a peak day of usage. Average annual per capita water use was 60 gallons per capita per day (pcpd) and average annual employee water use is currently 56 gallons pcpd. Since 2003, the City has seen a reduction of 20 percent in residential per capita use. Distribution system loss is approximately 4 percent for the three year rolling average ending in 2009. The Plan contains a six-year capital improvement plan with an estimated cost of approximately $5.6 million. In 2009, total revenues were $3.79 million and same year operating expenses were $3.42 million. The City identified funding sources for the proposed improvement projects which include rates, capital facility charges, loans, reserves and developer extension projects. Reclaimed Water and Regional Planning The City recognizes the value of reclaimed water as a means to conserve and extend the useful life of the potable water supply. The City worked with King County in the development of the regional reclaimed water planning process and has committed to work with its customers and the county as appropriate to assess the feasibility of using reclaimed water for various non-potable water needs. SEPA The City completed a State Environmental Policy Act (SEPA) checklist for the Plan and, as lead agency, issued a determination of non-significance for the issuance of the Plan on July 18, 2011. There were no appeals. |
| A review of the specific statutes, rules, codes, and policies to the water system plan is as follows: |
|  | A. General water plan, King County Code (KCC) 13.24.010 and 13.28 | Comments/findings |
| (1) | Review is applicable to utilities that obtain or distribute water in unincorporated King County under KCC 13.24. Is there a need to meet the consistency requirements of RCW 43.20.260? | Yes, the City of Bothell Water System Plan, February 2011, is subject to King County Council approval. Yes, the Washington State Department of Health (DOH) also needs to determine consistency of the Plan under RCW 43.20.260. |
| (2) | Consistency with King County Comprehensive Plan (KCCP) and development regulations, and policies including KCC 21A.28.040 development standards, provision of adequate supplies for anticipated growth and development. | Yes, the Plan is consistent. |
| (3) | Infrastructure for existing and future service areas based on adopted land use map. | Yes. The City used adopted land use maps for that portion of the service area within in unincorporated King County. |
| (4) | Review proposals for modified or expanded service areas based on compliance with utility’s approved plan, and ability to meet duty to serve requirement. | The service area is not expected to change. The City maintains duty to serve policies for its retail service area. |
| (5) | Sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes, the Plan demonstrates an ability to provide service consistent with applicable statutes, codes and regulations. The City obtains its water from the regional system and recently signed a long- term contract with Seattle Public Utilities. The city's water supplies are sufficient to meet projected peak day demand in 2030. |
| (6) | Monitor and review effectiveness of purveyor conservation plans if within area covered by an approved Coordinated Water System Plan (CWSP). | The City is within the East King County CWSP. The city's water use efficiency plan identifies conservation activities which the City employs as part of its long-range conservation plan. |
|  | B. Consistency requirements: 13.24.060 |  |
| (7) | State and local health requirements. | Yes. |
| (8) | Creation and maintenance of logical service areas. | Yes, the service area is logical. |
| (9) | Elimination or prevention of duplicate facilities. | Yes. The City intends to provide service within its service area by means of direct connection. The City maintains interties with neighboring utilities. |
| (10) | Promotion of most healthful and reliable services to the public. | Yes. Water purveyed by the City complies with public health standards. The water is chlorinated and fluoridated. |
| (11) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Yes, the city's rates for water service are comparable to the rates charged by similar utilities. The City has adopted a graduated rate structure to encourage efficient of water use. |
| (12) | KCCP and other pertinent county adopted plans and policies. | Yes, there is consistency between the city's Plan and the KCCP. |
| (13) | Basin-wide or multibasin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology (Ecology) or DOH. | No multibasin water plans are applicable. The City does not treat wastewater. The Plan is consistent with the East King County CWSP. |
| (14) | Applicable state water quality, water conservation, and waste management standards. | Yes, applicable standards are met. The city's per capita average consumption is 60 gallons per day. The three year rolling average distribution system leakage is estimated at 4 percent, which is below the ten percent requirement established under the Municipal Water Law. |
| (15) | Water Resources Act (RCW 90.54). | The Plan makes no connection with the requirements of RCW 90.54.180 or RCW 90.03.386. The City will maintain its existing conservation (efficiency) program to comply with DOH’s Water Use Efficiency Rule. |
| (16) | Growth Management Act (GMA) (RCW 36.70A). | The City received consistency statements from neighboring cities that its planning assumptions and data are consistent with their planning. The City's water service area includes unincorporated area and it appropriately used King County land use zoning for that area. |
| (17) | Groundwater management plans. | Not applicable. |
| (18) | Federally approved habitat conservation plans and recovery plans under the Endangered Species Act (ESA). | Not discussed in Plan. |
| (19) | Requirements for salmon recovery under Ch. 77.85 RCW, and other plans, including regional water supply or water resource management plans. | Not discussed in Plan. |
| (20) | Applicable requirements to evaluate opportunities for the use of reclaimed water under chapter 90.46 RCW and CO-7. | The Plan discusses reclaimed water, and recognizes the value of reclaimed water as a measure to conserve and extend the useful life of the potable water supply. The City did not complete the King County Reclaimed Water Checklist. However, the City participated with the county in its development of a regional reclaimed water plan and provided information similar to what would have been provided on the checklist. |
|  | C. King County Comprehensive Plan—consistency with provisions and specific policies (Water System Plan) |  |
|  | COUNTYWIDE PLANNING POLICIES |  |
| (21) | FW-5: management of resources for multiple beneficial uses, including flood and erosion hazard reduction. | Not applicable. |
| (22) | FW-12(c): ensure sufficient water supply for growth and fish habitat needs through long-term planning. | Sufficient water supply for projected growth is available. There is no apparent linkage and little relevance of the Plan to fish habitat needs. |
| (23) | CA-5, CA-6, and E-434 and policies to protect quantity and quality of groundwater. | The City uses surface water from the regional system. |
| (24) | CO-5: water supply shall be regionally coordinated. | The City obtains supply from the regional system and it is regionally coordinated. The City is located within the East King County Critical Water Supply Service Area, and its Plan is subject to consistency with the East King County CWSP. |
| (25) | CO-6: aggressive conservation efforts shall be implemented. | The City has a conservation program in place. The City states the conservation program meets minimum state requirements. |
|  | KING COUNTY COMPREHENSIVE PLAN POLICIES |  |
| (26) | F-102: King County will provide or manage countywide services, which include wastewater, water resource management, surface water management, flood warning and floodplain management, protection and preservation of natural resource lands. | Yes, for that portion of the service area that is in unincorporated King County. |
| (27) | F-104: plan for provision of services to rural areas. | The City service area does include portions of the urban unincorporated area and the City is committed to serving the area consistent with KCC. |
| (28) | F-105: King County to work with cities and service providers to establish priority areas for public funding of capital facilities. | The capital improvement program (CIP) is adequate and appropriately focused with funding sources identified. |
| (29) | F-201: all facilities and services should be provided in compliance with provisions and requirements of the ESA. | Not discussed in Plan. |
| (30) | F-202: ensure adequate supply of public facilities to support communities. | Yes, the City has sufficient water supplies. The City also maintains emergency interties with neighboring jurisdictions. |
| (31) | F-203: King County will work with cities, special purpose districts, and other service providers to define regional and local services and determine appropriate providers. | Yes. |
| (32) | F-208: support rural levels of development and not facilitate urbanization. | The City is committed to serving the area consistent with land use. |
| (33) | F-209 and F-212: capital facility plans and improvement programs for services to unincorporated King County are consistent with the KCCP. | Yes, the CIP is consistent with the KCCP. |
| (34) | F-210: King County helps coordinate development of utility facilities. | Yes, to the extent applicable, King County will do this. |
| (35) | F-215: King County shall initiate a sub-area planning process with any service provider that declares, in its capital facilities plan, an inability to meet service needs within service area. | Not applicable. The City did not identify any inability to meet service needs within its service area. |
| (36) | F-217: where an area-wide sewer, water, or transportation deficiency is identified, King County and applicable service providers shall remedy the deficiency through a joint planning process. | No area-wide water deficiency is identified. |
| (37) | F-225: King County supports coordination of regional water supply planning, sales of excess water among municipalities, water quality programs, and water conservation and reuse programs. | The City has agreements with its neighboring utilities for sharing of water during an emergency. |
| (38) | F-226: Group A water systems must meet duty to serve requirement within service area as defined under CWSP or by individual water system plans. | Yes, the City is committed to meeting its duty to serve in the retail service area. |
| (39) | F-227-231: provides a hierarchy of water supply providers in unincorporated King County, depending on whether within urban growth area or rural areas, with preference for providing water from existing suppliers. | The City recognizes its duty to serve within its service area and is committed to providing water to all its customers within its service area by direct connection. |
| (40) | F-237: King County supports the use of interties consistent with planning, and implementation of approved ESA and Clean Water Act response requirements. | The City maintains emergency interties with neighboring utilities. |
| (41) | F-239: King County partners with utilities to encourage best management practices and conservation through such means as developing reclaimed water, aggressive water conservation and reuse measures; support planned land uses with reliable service at minimum cost; encourage reclaimed water use, focused on large water users such as golf courses and cemeteries. | King County is willing to work with the City on these issues, particularly the evaluation of reclaimed water opportunities. |
| (42) | F-240: Utilities Technical Review Committee (UTRC) to consider (a) consistency with land use plans and development regulations; (b) approved or adopted plans for groundwater, ESA, salmon recovery, water resources, watershed planning, regional water supply plan; and (c) the Regional Wastewater Services Plan. | The UTRC did consider these issues and recommends approval of the Plan. |
| (43) | F-241: in reviewing proposals for modified and expanded service area boundaries, the UTRC must include an evaluation of the utility’s compliance with its comprehensive water system plan, including water conservation elements, and whether it can meet its duty to provide service; no approval of service area where unable to provide service for reasons in RCW 43.20.260. | The City is not planning to change its service area. |
| (44) | F-243: public drinking water system reservoirs and watersheds should be managed primarily to protect drinking water supplies, but allow multiple uses when not jeopardizing water quality; downstream uses including recreation, fish, and agricultural resources. | Not applicable. |
| (45) | F-244: groundwater supplies should be protected by preventing land uses that may adversely affect quantity or quality. | Not applicable. |