| Review of the City of Redmond 2011 Water System Plan, September 2011 |
| --- |
| Service Area The City of Redmond (City) service area within the Redmond city limits as well as unincorporated lands in King County. The area is approximately 10 miles east and northeast of Seattle at the north end of Lake Sammamish. Redmond is bordered by the City of Bellevue to the southwest; City of Kirkland to the west; and unincorporated King County to the north, east and southeast. The Union Hill Water Association is to the east and the Northeast Sammamish Sewer & Water District is to the southeast. The City provides water service in four distribution zones including the area served by the City wells (Well Service Area), two separate areas obtained in the past from water districts (Rose Hill and Overlake/Viewpoint Service Area) and the Redmond Ridge and Trilogy Urban Planned Developments (Novelty Hill Service Area). The service area is to be decreased with the possible transfer to Sammamish Plateau of an area originally in the Redmond Ridge master planned development. This area, which the City no longer wishes to serve, is located directly north of the City, is now separate from the urban portion of the Redmond Ridge master planned development, and is designated rural. The City does not currently provide service to the entire retail service area but plans to in the future. The City holds several franchises for water service, including franchises 9036, 12968, and 14424, which it is in the process of combining with the intent to create one franchise for water. Water Use Efficiency The City currently provides water service for approximately 60,000 people in its residential areas. During the business day, the population is approximately 100,000. The City has approximately 16,000 service connections. For 2005 – 2007, the annual average number of equivalent residential units was 36,694. The City has five wells, nine storage tanks (one shared with City of Bellevue and two with City of Kirkland) and a connection to the regional system via the Tolt River source and their participation with the Cascade Water Alliance. Approximately 30 percent of water demand is met by using the City's wells with the rest of the water coming from the regional system. The City has multiple operational and emergency interties with surrounding water purveyors. In 2009, the customers within the city's service area consumed approximately 7.0 million gallons of water per day (mgd) and 14.5 mgd during a peak day of usage. Distribution system loss was approximately 2.5 percent on average for 2005 – 2007 through over 320 miles of pipe. Build out demand is projected to be 14.3 mgd on an average day and 30.0 mgd peak day. The Plan contains a six-year capital improvement plan with an estimated cost of be approximately $14 million. The City identified funding sources for the proposed improvement projects includes rates, capital facility charges, loans, reserves and developer extension projects. Reclaimed Water and Regional Planning The City recognizes the value of reclaimed water as a means to conserve and extend the useful life of the potable water supply. The City worked with King County in the development of the regional reclaimed water planning process and has committed to work with its customers and the county as appropriate to assess the feasibility of using reclaimed water for various non-potable water needs. SEPA The City completed a State Environmental Policy Act (SEPA) checklist for the Plan and, as lead agency, issued a determination of non-significance for the issuance of the Plan on June 29, 2011. There were no appeals. |
| A review of the specific statutes, rules, codes, and policies to the water system plan is as follows: |
|  | A. General water plan, King County Code (KCC) 13.24.010 and 13.28 | Comments/findings |
| (1) | Review is applicable to utilities that obtain or distribute water in unincorporated King County under KCC 13.24. Is there a need to meet the consistency requirements of RCW 43.20.260? | Yes, the City of Redmond 2011 Water System Plan, September 2011 is subject to King County Council approval. Yes, the Washington State Department of Health (DOH) also needs to determine consistency of the Plan under RCW 43.20.260. |
| (2) | Consistency with King County Comprehensive Plan (KCCP) and development regulations, and policies including KCC 21A.28.040 development standards, provision of adequate supplies for anticipated growth and development. | Yes, the city's Plan is consistent. |
| (3) | Infrastructure for existing and future service areas based on adopted land use map. | Yes. The City used adopted land use maps for that portion of the service area within in unincorporated King County. |
| (4) | Review proposals for modified or expanded service areas based on compliance with utility’s approved plan, and ability to meet duty to serve requirement. | The service area is expected to change in small areas due to annexation and or agreements with neighboring jurisdictions. The City maintains duty to serve policies for its retail service area. |
| (5) | Sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes, the Plan demonstrates an ability to provide service consistent with applicable statutes, codes and regulations. The City obtains its water from groundwater sources and regional water through membership in the Cascade Water Alliance. The city's water supplies are sufficient to meet projected peak day demand in 2030. |
| (6) | Monitor and review effectiveness of purveyor conservation plans if within area covered by an approved Coordinated Water System Plan (CWSP). | The City is within the East King County CWSP. The city's water use efficiency plan identifies conservation activities which the City employs as part of its long-range conservation plan. |
|  | B. Consistency requirements: 13.24.060 |  |
| (7) | State and local health requirements. | Yes. |
| (8) | Creation and maintenance of logical service areas. | Yes, the service area is logical. |
| (9) | Elimination or prevention of duplicate facilities. | Yes. The City intends to provide service within its service area by means of direct connection. The City maintains interties with the City of Bellevue, City of Kirkland, Woodinville Water District, Union Hill Water Association, Northeast Sammamish Sewer and Water District, and Sammamish Plateau Water and Sewer District. The City shares one reservoir with the City of Bellevue and two reservoirs with the City of Kirkland. |
| (10) | Promotion of most healthful and reliable services to the public. | Yes. Water purveyed by the City complies with public health standards. The water is chlorinated and fluoridated. The existing combination of water sources provides sufficient capacity to meet the requirements of the City through 2030. |
| (11) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Yes, the city's rates for water service are comparable to the rates charged by similar utilities. The City has adopted a graduated rate structure to encourage efficient of water use. |
| (12) | KCCP and other pertinent county adopted plans and policies. | Yes, there is consistency between the city's Plan and the KCCP. |
| (13) | Basin-wide or multibasin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology (Ecology) or DOH. | No multibasin water plans are applicable. The City does not treat wastewater. The Plan is consistent with the East King County CWSP. |
| (14) | Applicable state water quality, water conservation, and waste management standards. | Yes, applicable standards are met. The City is in the process of completing a coliform monitoring program. The city's average day demand per equivalent residential unit (ERU) between 2006 and 2008 was 176 gallons per day. From 2005-2007, the average distribution system leakage was estimated at 2.5 percent, which is below the ten percent requirement established under the Municipal Water Law. |
| (15) | Water Resources Act (RCW 90.54). | The Plan makes no connection with the requirements of RCW 90.54.180 or RCW 90.03.386. The City will maintain its existing conservation (efficiency) program to comply with DOH’s Water Use Efficiency Rule. |
| (16) | Growth Management Act (GMA) (RCW 36.70A). | The City received consistency statements from neighboring cities that its planning assumptions and data are consistent with their planning. The City's water service area includes unincorporated area and it appropriately used King County land use zoning for that area. |
| (17) | Groundwater management plans. | The City owns 5 groundwater well sources and several monitoring wells. |
| (18) | Federally approved habitat conservation plans and recovery plans under the Endangered Species Act (ESA). | Not discussed in Plan. |
| (19) | Requirements for salmon recovery under Ch. 77.85 RCW, and other plans, including regional water supply or water resource management plans. | Not discussed in Plan. |
| (20) | Applicable requirements to evaluate opportunities for the use of reclaimed water under chapter 90.46 RCW and CO-7. | The Plan discusses reclaimed water, and recognizes the value of reclaimed water as a measure to conserve and extend the useful life of the potable water supply. However the City does not plan to invest in a reclaimed water distribution system at this time. The City did not complete the King County Reclaimed Water Checklist. However, the City participated with the county in its development of a regional reclaimed water plan and provided information similar to what would have been provided on the checklist. |
|  | C. King County Comprehensive Plan—consistency with provisions and specific policies (Water System Plan) |  |
|  | COUNTYWIDE PLANNING POLICIES |  |
| (21) | FW-5: management of resources for multiple beneficial uses, including flood and erosion hazard reduction. | Not applicable. |
| (22) | FW-12(c): ensure sufficient water supply for growth and fish habitat needs through long-term planning. | Sufficient water supply for projected growth is available. There is no apparent linkage and little relevance of the Plan to fish habitat needs. |
| (23) | CA-5, CA-6, and E-434 and policies to protect quantity and quality of groundwater. | The City uses groundwater and has implemented well head protection programs to protect groundwater quality. |
| (24) | CO-5: water supply shall be regionally coordinated. | The City is self supplied and obtains water from the regional system through Cascade Water Alliance. The City is located within the East King County Critical Water Supply Service Area, and its Plan is subject to consistency with the East King County CWSP. The service area for the City within the CWSP will need to be updated when the CWSP mapping of service areas is updated. |
| (25) | CO-6: aggressive conservation efforts shall be implemented. | The City has a conservation program in place. The City states the conservation program meets minimum state requirements. |
|  | KING COUNTY COMPREHENSIVE PLAN POLICIES |  |
| (26) | F-102: King County will provide or manage countywide services, which include wastewater, water resource management, surface water management, flood warning and floodplain management, protection and preservation of natural resource lands. | Yes, for that portion of the service area that is in unincorporated King County. |
| (27) | F-104: plan for provision of services to rural areas. | The City service area does include portions of the urban unincorporated area and the City is committed to serving the area consistent with King County’s Code. There is service to the rural area along the Old Redmond Road for a small number of isolated customers. Eventually the City would like to transfer these customers to some other utility, perhaps Union Hill. The City states it will continue to serve these customers but will not plan to provide any additional services. The area and services mentioned in the Plan are not demarcated as being within the retail service area of the City. |
| (28) | F-105: King County to work with cities and service providers to establish priority areas for public funding of capital facilities. | The capital improvement program (CIP) is adequate and appropriately focused with funding sources identified. |
| (29) | F-201: all facilities and services should be provided in compliance with provisions and requirements of the ESA. | Not discussed in Plan. |
| (30) | F-202: ensure adequate supply of public facilities to support communities. | Yes, the City has sufficient water supplies. The City also maintains emergency interties with neighboring jurisdictions. |
| (31) | F-203: King County will work with cities, special purpose districts, and other service providers to define regional and local services and determine appropriate providers. | Yes. |
| (32) | F-208: support rural levels of development and not facilitate urbanization. | The City is committed to serving the area consistent with land use. |
| (33) | F-209 and F-212: capital facility plans and improvement programs for services to unincorporated King County are consistent with the KCCP. | Yes, the CIP is consistent with the KCCP. |
| (34) | F-210: King County helps coordinate development of utility facilities. | Yes, to the extent applicable, King County will do this. |
| (35) | F-215: King County shall initiate a sub-area planning process with any service provider that declares, in its capital facilities plan, an inability to meet service needs within service area. | Not applicable. The City did not identify any inability to meet service needs within its service area. |
| (36) | F-217: where an area-wide sewer, water, or transportation deficiency is identified, King County and applicable service providers shall remedy the deficiency through a joint planning process. | No area-wide water deficiency is identified. |
| (37) | F-225: King County supports coordination of regional water supply planning, sales of excess water among municipalities, water quality programs, and water conservation and reuse programs. | The City has agreements with its neighboring utilities for sharing of water during an emergency. |
| (38) | F-226: Group A water systems must meet duty to serve requirement within service area as defined under CWSP or by individual water system plans. | Yes, the City is committed to meeting its duty to serve in the retail service area. |
| (39) | F-227-231: provides a hierarchy of water supply providers in unincorporated King County, depending on whether within urban growth area or rural areas, with preference for providing water from existing suppliers. | The City recognizes its duty to serve within its service area and is committed to providing water to all its customers within its service area by direct connection. The City may consider indirect service within the future service area. |
| (40) | F-237: King County supports the use of interties consistent with planning, and implementation of approved ESA and Clean Water Act response requirements. | The City is 30 percent self supplied with the rest of its water coming from the regional water supply. The City maintains emergency interties with neighboring utilities. |
| (41) | F-239: King County partners with utilities to encourage best management practices and conservation through such means as developing reclaimed water, aggressive water conservation and reuse measures; support planned land uses with reliable service at minimum cost; encourage reclaimed water use, focused on large water users such as golf courses and cemeteries. | King County is willing to work with the City on these issues, particularly the evaluation of reclaimed water opportunities. |
| (42) | F-240: Utilities Technical Review Committee (UTRC) to consider (a) consistency with land use plans and development regulations; (b) approved or adopted plans for groundwater, ESA, salmon recovery, water resources, watershed planning, regional water supply plan; and (c) the Regional Wastewater Services Plan. | The UTRC did consider these given issues and recommends approval of the Plan. |
| (43) | F-241: in reviewing proposals for modified and expanded service area boundaries, the UTRC must include an evaluation of the utility’s compliance with its comprehensive water system plan, including water conservation elements, and whether it can meet its duty to provide service; no approval of service area where unable to provide service for reasons in RCW 43.20.260. | The City is not planning to change its service area. |
| (44) | F-243: public drinking water system reservoirs and watersheds should be managed primarily to protect drinking water supplies, but allow multiple uses when not jeopardizing water quality; downstream uses including recreation, fish, and agricultural resources. | The City jointly owns one water storage reservoir with City of Bellevue and two with the City of Kirkland. |
| (45) | F-244: groundwater supplies should be protected by preventing land uses that may adversely affect quantity or quality. | Yes, this is done by the City. |