Review of the Union Hill Water Association’s Comprehensive Water System Plan

Service Area The Union Hill Water Association was formed in 1966. It is a private, non-profit, cooperative located in central King County southeast of the City of Redmond and northeast of Lake Sammamish. Union Hill’s service area is generally bounded by the City of Redmond, Northeast Sammamish Sewer and Water District, and Sammamish Plateau Water and Sewer District. The service area is comprised of 5,770 acres (approximately 9 square miles) of land and is not expected to significantly change in the future. The water system currently serves a residential population of approximately 4,958 people, and an employment, or transitory population of 1,886 through 2,054 service connections. The 2033 projected population is 9,185 with an employment base of 2,806 people. Union Hill is in the process of updating its franchise with the County. Union Hill uses two ground water wells for the primary sources of supply. The distribution system includes approximately 56 miles of pipe, 4 reservoirs with a combined storage of 6.5 million gallons, and three booster pump stations and 5 pressure zones. During extreme demand Union Hill purchases water via interties. The Plan contains a modest capital improvement program. Reclaimed Water Union Hill does not receive or use reclaimed water but is willing to work with King County to identify opportunities and has completed the King County Reclaimed Water Checklist. SEPA Union Hill completed a State Environmental Policy Act (SEPA) checklist for the Plan. The King County Department of Natural Resources and Parks as lead agency under SEPA issued a determination of non-significance for the approval of the Plan on January 13, 2015. There were no appeals.

|  | A. General water plan specific King County Code (KCC) 13.24.010 | Comments/findings |
| --- | --- | --- |
| (1) | The code is applicable to water and or sewer utilities that obtain water in unincorporated areas, provide service in unincorporated areas of King County, and/or are component agencies of the regional wastewater system. | Union Hill both obtains and distributes water in unincorporated areas of King County and so review under KCC 13.24 is appropriate. |
| (2) | Water system plans should be submitted every six years or sooner if required by the Washington State Department of Health. | The last Union Hill Plan was approved by King County in 2005. Union Hill will seek Plan approval from the Washington State Department of Health. |
| (3) | The infrastructure for existing and future service areas based on adopted land use map. | Yes, within the water planning area, land use and zoning are designated by two jurisdictions: King County and the City of Redmond. King County land use and zoning was appropriately used in determining the water demand projections. |
| (4) | The Plan contains sufficient information to demonstrate the ability to provide services consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes, the Plan demonstrates that Union Hill has ample water supply to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. |
| (5) | The Plan is consistent with Washington Administrative Code (WAC) 246-290-100 for the water service. | Yes, the Plan is consistent with the applicable rules. |
|  | B. Consistency requirements: 13.24.060 |  |
| (6) | King County Code related to the installation of fire hydrants and water mains. | Yes, the Plan references KCC 17.08 and proposes to provide adequate fire flow. |
| (7) | State and local health requirements. | The Plan has not yet been approved by the Washington State Department of Health. The UTRC review process included a representative of Public Health-Seattle and King County. |
| (8) | Elimination or prevention of duplicate facilities. | Union Hill has written agreements with other water providers regarding areas to be served in order to avoid overlapping jurisdiction and to ensure efficiency in the use of existing facilities. |
| (9) | Promotion of most healthful and reliable services to the public. | Yes. |
| (10) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Currently, Union Hill charges for water are in the affordable range. |
|  | C: King County Comprehensive Plan – consistency with provisions and specific policies. |  |
| (11) | Consistency with the King County Comprehensive Plan and applicable County plans and policies including the Flood Hazard Management Plan and Emergency Response Plan. | Yes, the Plan is consistent with the applicable comprehensive plans. |
| (12) | Consistency with the Coordinated Water System Plans adopted in KCC 13.28. | Yes, the Plan is consistent with the East King County Coordinated Water System Plan (CWSP). The Union Hill CWSP designated service area boundary is concurrently its future and Retail Service Area. |
| (13) | Basin-wide or multi-basin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology or the Washington State Department of Health. | Not applicable. |
| (14) | Applicable state water quality, water conservation (e.g., chapter 90.54 RCW and RCW 90.48.495), and waste management standards. | Yes. Union Hill implements a water conservation program. In October of 2011, a routine water sample tested positive for fecal coliform. Repeat samples could not replicate the positive test and it was deemed sampling error. |
| (15) | Growth Management Act; chapter 36.70A RCW. | Yes, the Plan is consistent with the Growth Management Act. |
| (16) | Groundwater Management Plans. | The Plan references groundwater protection as one of its goals. A Wellhead Protection Program was developed for the well field. |
| (17) | Federally-approved habitat conservation plans and recovery plans under Endangered Species Act, and other plans, including regional water supply or water resource management plans. | Union Hill is aware of, and supports, the planning done for salmon recovery purposes. There is no active applicable regional water supply plan. |
| (18) | Applicable requirements to evaluate opportunities for the use of reclaimed water under chapter 90.46 RCW. | Yes, Union Hill supports King County’s reclaimed water planning efforts. Union Hill evaluated reclaimed water by completing the King County Reclaimed Water Checklist. |
| (19) | State Environmental Policy Act documentation. | Union Hill is not eligible to make its own SEPA determination and provided the County with a completed SEPA checklist. The County issued a Determination of Nonsignificance for approval of the plan on January 13, 2015, with no appeals. |
|  | COUNTYWIDE PLANNING POLICIES |  |
| (20) | DP‐13: All jurisdictions shall plan to accommodate housing and employment targets. This includes: “Coordinating water, sewer, transportation and other infrastructure plans and investments among agencies, including special purpose districts;…”. | The Union Hill system is in the rural area and has appropriately considered housing and employment targets. |
| (21) | PF‐4: Develop plans for long‐term water provision to support growth and to address the potential impacts of climate change on regional water resources. | Union Hill has a reasonable plan for long-term water supply to meet projected growth. The Plan does not discuss climate change impacts on water supply. |
| (22) | PF‐5: Support efforts to ensure that all consumers have access to a safe, reliably maintained, and sustainable drinking water source that meets present and future needs. | Yes, the system does this. |
| (23) | PF‐6: Coordinate water supply among local jurisdictions, tribal governments, and water purveyors to provide reliable and cost‐effective sources of water for all users, including residents, businesses, fire districts, and aquatic species. | Not applicable. |
| (24) | PF‐7: Plan and locate water systems in the Rural Area that are appropriate for rural uses and densities and do not increase the development potential of the Rural Area. | Union Hill serves a rural area and appropriately used King County land use and zoning guidelines. |
| (25) | PF‐8: Recognize and support agreements with water purveyors in adjacent cities and counties to promote effective conveyance of water supplies and to secure adequate supplies for emergencies. | Union Hill has agreements with neighboring utilities for service area and to assist in emergency situations. |
| (26) | PF‐9: Implement water conservation and efficiency efforts to protect natural resources, reduce environmental impacts, and support a sustainable long‐term water supply to serve the growing population. | The Union Hill average day water demand over the historical period for a single-family residence is 270 gallons per day. The ratio of maximum day demand to average day demand has ranged from 2.55 to 3.37 for the period of record. The Union Hill three-year average distribution system loss is 17.7 percent and exceeds the state standard of 10 percent. The system will be developing a water loss control plan. |
| (27) | PF‐10: Encourage water reuse and reclamation, especially for high‐volume non‐potable water users such as parks, schools, and golf courses. | Union Hill is partially located within the sewer service area of King County’s Wastewater Treatment Division. There are no opportunities to use reclaimed water at this time. |
|  | KING COUNTY COMPREHENSIVE PLAN POLICIES |  |
| (28) | F-107: Plan for provision of services to rural areas. | Union Hill provides water to the rural area. |
| (29) | F-108: King County to work with cities and service providers to establish priority areas for public funding of capital facilities. | The capital improvement program (CIP) is adequate and appropriately focused with funding sources identified. |
| (30) | F-201: All facilities and services should be provided in compliance with provisions and requirements of the Endangered Species Act (ESA) and the Clean Water Act. | Yes, to the extent known, facilities and service are provided consistent with the federal laws. |
| (31) | F-209: Support rural levels of development and not facilitate urbanization. | Yes, the water system supports rural levels of development and will not facilitate urbanization. |
| (32) | F-210: Capital facility plans and improvement programs for services to unincorporated King County are consistent with the KCCP. | Yes, the CIP is consistent with the KCCP. |
| (33) | F-211: King County helps coordinate development of utility facilities. | Yes, to the extent applicable, King County will do this. |
| (34) | F-221: King County shall initiate a sub-area planning process with any service provider that declares, in its capital facilities plan, an inability to meet service needs within service area. | Not applicable. Union Hill did not identify any inability to meet service needs within its service area. |
| (35) | F-223: If a service deficiency is identified in a service provider's existing service area, King County and the applicable service provider shall remedy the deficiency through a joint planning process addressing capital improvement programs and long-term funding strategies reuse programs. | Not applicable. Union Hill did not identify any inability to meet service needs within its service area. |
| (36) | F-231: King County supports coordination of regional water supply planning, sales of excess water supplies among municipalities in the region, water quality programs and water conservation, reuse and reclaimed water programs. | Yes, Union Hill supports regional water supply coordination. |
| (37) | F-232: Water utilities that obtain water from, or distribute water in unincorporated King County, and water utilities formed as special purpose districts under Title 57 RCW are required to submit water system plans to the County for review and approval and shall describe in their plans how they intend to meet their duty to provide service within their retail service areas. | Union Hill obtains and distributes water in unincorporated King County so the plan is subject to review and approval by the King County Council. Union Hill is committed to meeting its duty to serve in its retail service area by direct service and has described its general terms of service in the Plan. |
|  | F-248 King County shall partner with utilities to publicize water conservation and encourage best management practices that conserve potable water supply through measures that include use of alternative supplies such as reclaimed water. | Yes, the County will do this. |
| (38) | F-246: King County supports interties that allow the transfer of water resources among water utilities to meet the projected demands for growth where such interties meet the requirements of RCW 90.03.383 and are also consistent with any applicable locally adopted comprehensive plans, regional water supply plans, adopted groundwater management plans, watershed plans, approved Coordinated Water System Plans, ESA response requirements and Clean Water Act requirements. | Union Hill has one intertie with Northeast Sammamish Sewer and Water District, one intertie with the City of Redmond for emergency supply, two interties with Redmond Ridge for emergency supply and two interties with Sammamish Plateau Water and Sewer District interties. |
| (39) | F-249: Utilities with more than one thousand service connections required to submit water system plans for approval to King County shall include an evaluation of reclaimed water use opportunities by completing King County’s Water Reclamation Evaluation. | Union Hill completed King County’s Water Reclamation Evaluation Checklist. There are no opportunities for use of reclaimed water at this time. |
| (40) | F-251: In its review of water system plans, the UTRC shall consider the criteria provided in KCC 13.24.010, 13.24.060, and 13.24.070, and determine the plan’s consistency with the following: a. Applicable provisions of the King County Comprehensive Plan, land use plans, and development regulations adopted under the Growth Management Act; b. Approved or adopted regional water resource plans, such as basin plans, groundwater plans, watershed-based conservation and recovery plans developed under ESA, salmon recovery plans developed under chapter 77.85 RCW, water resource plans developed under chapter 90.54 RCW, watershed plans developed under chapter 90.82 RCW, and a regional water supply plan or water resource management plan; c. The County’s Regional Wastewater Services Plan; and d. Other applicable provisions of countywide plans managed by King County, as specified in UTRC Guidance or checklists. | The UTRC did consider these issues and recommends approval of the Plan. |
| (41) | F-252: In reviewing proposals for modified and expanded service area boundaries for municipal water suppliers, the UTRC shall consider, in addition to Policy F-251: a. Compliance by the water system with its water system comprehensive plan, including water conservation elements; b. Whether it can meet its duty to provide service within its service area, as required under chapter 43.20 RCW; and c. Consistency with the service provisions of any applicable Coordinated Water System Plan, as adopted in King County Code Chapter 13.28. | Union Hill has made minor modifications to its service area is not planning to change its service area. Service area analysis shows some overlapping areas between Union Hill and the City of Redmond. Depending on the expansion of Union Hill and Redmond’s water systems, the areas in question are along 196th AVE NE and the north and northwest corner of Union Hill’s service boundary. Future service will be negotiated in these areas based on the closest available water and least cost of providing the infrastructure to serve such development. |
| (42) | F-253: Consistent with Countywide Planning Policies, public drinking water system surface water reservoirs and their watersheds should be managed primarily for the protection of drinking water, but should allow for multiple uses, including recreation, when such uses do not jeopardize drinking water quality standards. Public watersheds must be managed to protect downstream fish and agriculture resources. | Not applicable. |
| (43) | F-254: Groundwater-based public water supplies should be protected by preventing land uses that may adversely affect groundwater quality or quantity to the extent that the supply might be jeopardized. The County shall protect the quality and quantity of groundwater used as water supplies through implementation of Policies E-493 through E-497 where applicable. | Yes, Union Hill prepared a Wellhead Protection Program which has been incorporated into the County’s critical areas ordinance. |