Review of the Mirrormont Water System Individual Water System Plan

Service Area The Mirrormont Water System (Mirrormont) is owned and operated by the Washington Water Service Company, a private for-profit company. Mirrormont is located in central King County, approximately 4½-miles south of the City of Issaquah along the eastern slope of the Issaquah Creek Valley and east of the City of Renton. Mirrormont is generally bounded by the Cedar River Water & Sewer District to the south, Four Lake Landowners Association to the southwest, and Tiger Mountain Tracts Water System to the north. The service area comprises approximately 3.8 square miles. The area is primarily single-family residential with a few multi-family units. The service area is not expected to significantly change in the future. The water system currently serves a population of approximately 1,918 people through 770 service connections; the system is approved to serve up to 916 connections. Mirrormont is in the process of updating its franchise with the County. Mirrormont uses both spring water and ground water for supply to the distribution system which includes the Tiger Mountain spring, five wells, three reservoirs, three pump stations, 8 pressure-reducing stations, and twelve pressure zones. The Plan contains a modest capital improvement program. Reclaimed Water Mirrormont does not receive or use reclaimed water but is willing to work with King County to identify opportunities. SEPA Mirrormont completed a State Environmental Policy Act (SEPA) checklist for the Plan. The King County Department of Natural Resources and Parks, as lead agency under SEPA, issued a determination of non-significance for the approval of the Plan on December 9, 2014. There were no appeals.

|  | A. General, water and sewer plan specific King County Code (KCC) 13.24.010 | Comments/findings |
| --- | --- | --- |
| (1) | The code is applicable to water and or sewer utilities that obtain water in unincorporated areas, provide service in unincorporated areas of King County, and/or are component agencies of the regional wastewater system. | Mirrormont both obtains and distributes water in unincorporated areas of King County and so review under KCC 13.24 is appropriate. |
| (2) | Water system plans should be submitted every six years or sooner if required by the Washington State Department of Health. | The last Mirrormont plan was approved by King County in 2005. Mirrormont will seek plan approval from the Washington State Department of Health. |
| (3) | The infrastructure for existing and future service areas based on adopted land use map. | Yes, King County land use and zoning was appropriately used in determining the water demand projections. |
| (4) | The Plan contains sufficient information to demonstrate the ability to provide services consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes, the Plan demonstrates that Mirrormont has ample water supply to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. |
| (5) | The Plan is consistent with Washington Administrative Code (WAC) 246-290-100 for the water service. | Yes, the Plan is consistent with the applicable rules. |
|  | B. Consistency requirements: 13.24.060 |  |
| (6) | King County Code related to the installation of fire hydrants and water mains. | Yes, the Plan references KCC 17.08 and proposes to provide adequate fire flow. |
| (7) | State and local health requirements. | The Plan has not yet been approved by the Washington State Department of Health. The UTRC review process included a representative of Public Health-Seattle and King County. |
| (8) | Elimination or prevention of duplicate facilities. | Mirrormont has written agreements with other water providers regarding areas to be served in order to avoid overlapping jurisdiction and to ensure efficiency in the use of existing facilities. |
| (9) | Promotion of most healthful and reliable services to the public. | Yes. |
| (10) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Currently, Mirrormont charges a rate that is in the affordable range. As a private for-profit water system Mirrormont is regulated by the Washington State Utilities and Transportation Commission. |
|  | C: King County Comprehensive Plan – consistency with provisions and specific policies |  |
| (11) | Consistency with the King County Comprehensive Plan and applicable County plans and policies including the Flood Hazard Management Plan and Emergency Response Plan. | Yes, the Plan is consistent with the applicable comprehensive plans. |
| (12) | Consistency with the Coordinated Water System Plans adopted in KCC 13.28 | Yes, the Plan is consistent with the East King County Coordinated Water System Plan (CWSP) except for the desire of Mirrormont to modify the CWSP boundaries through the approval of this plan. The approval of this plan does not modify the CWSP boundary. Rather, that boundary will be modified or changed when the CWSP is updated. Within this plan update Mirrormont identified two parcels served by Tiger Mountain Tracts water system within its CWSP service area and modified its boundary to resolved that conflict. The Mirrormont CWSP designated service area boundary is concurrently its future and Retail Service Area. |
| (13) | Basin-wide or multi-basin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology or the Washington State Department of Health. | Not applicable. |
| (14) | Applicable state water quality, water conservation (e.g., chapter 90.54 RCW and RCW 90.48.495), and waste management standards. | Yes. Mirrormont implements a water conservation program. |
| (15) | Growth Management Act; chapter 36.70A RCW. | Yes, the Plan is consistent with the Growth Management Act. See specific policies below. |
| (16) | Groundwater Management Plans. | The Plan references groundwater protection as one of the goals of the plan. A Wellhead Protection Program was developed for the existing well field. |
| (17) | Federally-approved habitat conservation plans and recovery plans under Endangered Species Act, and other plans, including regional water supply or water resource management plans. | Mirrormont is aware of, and supports, the planning done for salmon recovery purposes. There is no active applicable regional water supply plan. |
| (18) | Applicable requirements to evaluate opportunities for the use of reclaimed water under chapter 90.46 RCW. | Yes, Mirrormont supports King County’s reclaimed water planning efforts. |
| (19) | State Environmental Policy Act documentation. | Mirrormont is not eligible to make its own SEPA determination. Mirrormont provided the County a completed SEPA checklist. The County issued a Determination of Nonsignificance for approval of the plan on December 9, 2014, with no appeals. |
|  | COUNTYWIDE PLANNING POLICIES |  |
| (20) | DP‐13: All jurisdictions shall plan to accommodate housing and employment targets. This includes: “Coordinating water, sewer, transportation and other infrastructure plans and investments among agencies, including special purpose districts;…”. | The Mirrormont system is in the rural area and has appropriately considered housing and employment targets. |
| (21) | PF‐4: Develop plans for long‐term water provision to support growth and to address the potential impacts of climate change on regional water resources. | Mirrormont has a reasonable plan for long-term water supply to meet projected growth. The plan does not discuss climate change impacts on water supply. |
| (22) | PF‐5: Support efforts to ensure that all consumers have access to a safe, reliably maintained, and sustainable drinking water source that meets present and future needs. | Yes, the system does this. |
| (23) | PF‐6: Coordinate water supply among local jurisdictions, tribal governments, and water purveyors to provide reliable and cost‐effective sources of water for all users, including residents, businesses, fire districts, and aquatic species. | Not applicable. |
| (24) | PF‐7: Plan and locate water systems in the Rural Area that are appropriate for rural uses and densities and do not increase the development potential of the Rural Area. | Mirrormont serves a rural area and appropriately used King County land use and zoning. |
| (25) | PF‐8: Recognize and support agreements with water purveyors in adjacent cities and counties to promote effective conveyance of water supplies and to secure adequate supplies for emergencies. | Mirrormont has agreements with neighboring utilities for service area and to assist in emergency situations. |
| (26) | PF‐9: Implement water conservation and efficiency efforts to protect natural resources, reduce environmental impacts, and support a sustainable long‐term water supply to serve the growing population. | Mirrormont average day water demand has decreased from 293 gallons/day/equivalent residential unit (ERU) in 2004 to 244 gallons/day/ERU in 2012. Mirrormont’s three-year average distribution system loss is 16.4 percent since 2012 and exceeds the state standard of 10 percent. The system will be developing a water loss control plan. |
| (27) | PF‐10: Encourage water reuse and reclamation, especially for high‐volume non‐potable water users such as parks, schools, and golf courses. | Mirrormont is not located within the service area of the King County Wastewater Treatment Division’s sewer service area. There are no opportunities to use reclaimed water. |
|  | KING COUNTY COMPREHENSIVE PLAN POLICIES |  |
| (28) | F-107: Plan for provision of services to rural areas. | Mirrormont provides water to the rural area. |
| (29) | F-108: King County to work with cities and service providers to establish priority areas for public funding of capital facilities. | The capital improvement program (CIP) is adequate and appropriately focused with funding sources identified. |
| (30) | F-201: All facilities and services should be provided in compliance with provisions and requirements of the Endangered Species Act and the Clean Water Act. | Yes, to the extent known, facilities and service are provided consistent with the federal laws. |
| (31) | F-209: Support rural levels of development and not facilitate urbanization. | Yes, the water system supports rural levels of development and will not facilitate urbanization. |
| (32) | F-210: Capital facility plans and improvement programs for services to unincorporated King County are consistent with the KCCP. | Yes, the CIP is consistent with the KCCP. |
| (33) | F-211: King County helps coordinate development of utility facilities. | Yes, to the extent applicable, King County will do this. |
| (34) | F-221: King County shall initiate a sub-area planning process with any service provider that declares, in its capital facilities plan, an inability to meet service needs within service area. | Not applicable. Mirrormont did not identify any inability to meet service needs within its service area. |
| (35) | F-223: If a service deficiency is identified in a service provider's existing service area, King County and the applicable service provider shall remedy the deficiency through a joint planning process addressing capital improvement programs and long-term funding strategies reuse programs. | Not applicable. Mirrormont did not identify any inability to meet service needs within its service area. |
| (36) | F-231: King County supports coordination of regional water supply planning, sales of excess water supplies among municipalities in the region, water quality programs and water conservation, reuse and reclaimed water programs. | Yes, Mirrormont supports regional water supply coordination. |
| (37) | F-232: Water utilities that obtain water from, or distribute water in unincorporated King County, and water utilities formed as special purpose districts under Title 57 RCW are required to submit water system plans to the County for review and approval and shall describe in their plans how they intend to meet their duty to provide service within their retail service areas. | Mirrormont obtains and distributes water in unincorporated King County so the plan is subject to review and approval by the King County Council. Mirrormont is committed to meeting its duty to serve in its retail service area by direct service and has described in the plan its general terms of service. |
|  | F-248 King County shall partner with utilities to publicize water conservation and encourage best management practices that conserve potable water supply through measures that include use of alternative supplies such as reclaimed water. | Yes, the County will do this. |
| (38) | F-246: King County supports interties that allow the transfer of water resources among water utilities to meet the projected demands for growth where such interties meet the requirements of RCW 90.03.383 and are also consistent with any applicable locally adopted comprehensive plans, regional water supply plans, adopted groundwater management plans, watershed plans, approved Coordinated Water System Plans, Endangered Species Act (ESA) response requirements and Clean Water Act requirements. | Mirrormont has no interties with other utilities. |
| (39) | F-249: Utilities with more than one thousand service connections required to submit water system plans for approval to King County shall include an evaluation of reclaimed water use opportunities by completing King County’s Water Reclamation Evaluation. | Mirrormont has less than 1,000 service connections and did not complete King County’s Water Reclamation Evaluation Checklist. |
| (40) | F-251: In its review of water system plans, the UTRC shall consider the criteria provided in KCC 13.24.010, 13.24.060, and 13.24.070, and determine the plan’s consistency with the following: a. Applicable provisions of the King County Comprehensive Plan, land use plans, and development regulations adopted under the Growth Management Act; b. Approved or adopted regional water resource plans, such as basin plans, groundwater plans, watershed-based conservation and recovery plans developed under ESA, salmon recovery plans developed under chapter 77.85 RCW, water resource plans developed under chapter 90.54 RCW, watershed plans developed under chapter 90.82 RCW, and a regional water supply plan or water resource management plan; c. The County’s Regional Wastewater Services Plan; and d. Other applicable provisions of countywide plans managed by King County, as specified in UTRC Guidance or checklists. | The UTRC did consider these issues and recommends approval of the Plan. |
| (41) | F-252: In reviewing proposals for modified and expanded service area boundaries for municipal water suppliers, the UTRC shall consider, in addition to Policy F-251: a. Compliance by the water system with its water system comprehensive plan, including water conservation elements; b. Whether it can meet its duty to provide service within its service area, as required under chapter 43.20 RCW; and c. Consistency with the service provisions of any applicable Coordinated Water System Plan, as adopted in King County Code Chapter 13.28. | Mirrormont has made minor modifications to its service area is not planning to change its service area. The 1992 Mirrormont CWSP service area is not parcel specific, cuts through the middle of a several parcels and overlapped several known Group A water systems. In any event, Mirrormont desires to modify its service area to eliminate bisected parcels and overlap with known Group A water systems. |
| (42) | F-253: Consistent with Countywide Planning Policies, public drinking water system surface water reservoirs and their watersheds should be managed primarily for the protection of drinking water, but should allow for multiple uses, including recreation, when such uses do not jeopardize drinking water quality standards. Public watersheds must be managed to protect downstream fish and agriculture resources. | Not applicable. |
| (43) | F-254: Groundwater-based public water supplies should be protected by preventing land uses that may adversely affect groundwater quality or quantity to the extent that the supply might be jeopardized. The county shall protect the quality and quantity of groundwater used as water supplies through implementation of Policies E-493 through E-497 where applicable. | Yes, Mirrormont prepared a Wellhead Protection Program which has been incorporated into the County’s critical areas ordinance. |