SPU/DNRP Shared West Ship Canal Tunnel

Project Description

February 19, 2015

Project Purpose

The purpose of the Shared West Ship Canal Tunnel (Tunnel) is to provide offline storage of CSO flows for two Seattle Public Utilities (SPU) and two King County Department of Natural Resources and Parks (DNRP) DNRPCSO basins to meet regulatory control standards which limits CSOs to an average of no more than one untreated discharge per year per outfall on a twenty year moving average. The specific basins and CSO to be controlled by the Tunnel include the SPU Ballard CSO basins (NPDES 150/151, NPDES 152), Fremont/Wallingford CSO basins (NPDES 147, NPDES 174), DNRP 3rd Avenue West Regulator (DSN008), and DNRP 11th Avenue NW Regulator (DSN004). The total control volume to be achieved for both SPU and DNRP CSO basins is 15.24 million gallons (MG). The SPU and DNRPDNRP CSOs described here do not currently meet the State’s standard of control. The facility must also meet water quality standard and be verified by post construction monitoring (sediment sampling). The SPU and DNRP CSOs described here do not currently meet the Federal and State standards.

Project Scope

Offline storage will be provided with a deep storage tunnel constructed between the Ballard and Fremont/Wallingford CSO areas, on the north side of the Ship Canal. The Shared West Ship Canal Tunnel will control the Ballard CSO basins (NPDES 150/151, NPDES 152), Fremont/Wallingford CSO basins (NPDES 147, NPDES 174), DNRP 3rd Avenue West Regulator (DSN008), and 11th Avenue NW Regulator (DSN004). The total control volume for both SPU and DNRP CSO basins is 15.24 MG. Figure 1 provides a plan view of the project location and components.

The main components of the Shared West Ship Canal Tunnel include the storage tunnel and appurtenances, conveyance facilities to convey SPU and DNRP CSO flows into the tunnel, and a tunnel pumping effluent line to drain flows away from the tunnel.  A description of each component is as follows:

The storage tunnel and appurtenances will include:

- A bored 15.24-MG offline storage tunnel with a nominal 14 feet inside diameter and nominally 14,000 feet long;

  - The stored volume in the storage tunnel will flow from the Fremont/Wallingford CSO Outfall 147 westward to an effluent pump station located near the Ballard CSO Outfall 152.

  - The tunnel route is planned to be generally in street rights-of-way along north side of the Ship Canal

- Six diversion structures for diverting influent CSO flow away from existing CSO outfalls to the Tunnel;

- Four drop structures to convey influent CSO flow into the storage tunnel;

- An East Tunnel Portal with an approximate tunnel invert elevation of 54-feet (Seattle datum) housing odor control equipment; and,

- A West Tunnel Portal with an approximate tunnel invert elevation of 70-feet (Seattle datum) housing an effluent pump station with a peak capacity of 32 MGD to empty the storage tunnel in approximately 12 hours.

Conveyance facilities, included in the Shared WSCT, from SPU and DNRP CSOs will include:

- Approximately 100 lineal feet (lf) of 36 -inch diameter gravity sewer line to convey flows from SPU’s Fremont CSO area (NPDES 174).  Approximately 2,400 lineal feet (lf) of 42 to 72-inch diameter gravity sewer line to convey flows from SPU’s Ballard and Wallingford CSO areas (NPDES 150/151, NPDES 152, and NPDES 147 respectively) have been excluded from the shared project.

- Approximately 900 lf of 48 to 60-inch diameter gravity sewer line to convey flows from DNRP’s 3rd Ave. W. and 11th Ave. NW CSO to tunnel drop structures.  Approximately 800 lf of the gravity sewer line will be under the Ship Canal to connect the 3rd Ave. W. diversion structure to the Tunnel.

The Tunnel pumping station effluent line will consist of an approximately 1,900 lf force main to discharge the stored tunnel CSO flows directly into DNRP’s existing Ballard Siphon wet-weather barrel forebay.

The control strategy will limit the inflow to the tunnel from each outfall to each outfall’s control volume per event. The control volume for each outfall is:

- Fremont/Wallingford (NPDES 174): 1.06 MG

- Fremont/Wallingford (NPDES 147): 2.15 MG

- Ballard (NPDES 152): 5.38 MG

- Ballard (NPDES 150/151): 0.62 MG

- 3rd Avenue West (DSN008): 4.18 MG

- 11th Avenue Northwest (DSN004): 1.85 MG

Each agency has calculated the control volumes required to meet their independent needs. Although calculation methods vary between the agencies, SPU and DNRP agree that these are the volumes to be controlled to and provided for by the tunnel project.

SPU will own and operate all of the Tunnel components. SPU’s ownership begins and DNRP’s ownership ends where DNRP’s system connects to the upstream wall of SPU’s new diversion structures associated with the 3rd Avenue West and 11th Ave Northwest outfalls. The Tunnel components include:

- The tunnel in its entirety, including the East and West Portals

- The pump station and force main

- All diversion structures, including the 3rd Avenue West and 11th Ave West diversion structures

- All of the conveyance system associated with SPU’s outfalls and downstream of the 3rd Avenue West and 11th Ave West diversion structures

- All control gates into the tunnel and associated structures and control systems

- All odor control systems

- And all appurtenances associated with the above.

Any changes to this project scope need to be negotiated and agreed to by both SPU and DNRP.

Figure 1: Shared West Ship Canal Tunnel Plan

Project Schedule Summary

The schedule of major project milestones is summarized below.  The summary is based on the detailed scheduled contained in Attachment 9 to the Final Project Definition Report, Volume 1, issued by SPU in December 2014.

| Task | Approximate Start Date | Approximate Completion Date |
| --- | --- | --- |
| Options Analysis Complete | Ongoing | April 2015 |
| Complete Final Facility Plan | Ongoing | December 2017 |
| 30% Design for Storage | February 2016 | June 2016 |
| 60% Design for Storage | July 2016 | January 2017 |
| 90% Design for Storage | February 2017 | May 2017 |
| Final Design for Storage | October 2017 | December 2017 |
| Permitting for Storage | January 2017 | January 2018 |
| Storage Construction | January 2018 | November 2023 |
| Substantial Completion |  | December 2023 |
| Commissioning and System Integration | August 2022 | June 2025 |
| Storage Closeout | June 2025 | October 2026 |
| Achieve Controlled Status |  | October 2026 |

# Signatures

| SPU Rep | Title |
| --- | --- |
|  | Date: |
| Pam Elardo, P.E. | Director, King County Wastewater Treatment Division |
|  | Date: |