| Review of the Lake Forest Park Water District Comprehensive Water System Plan 2016 (the Plan) |
| --- |
| Service Area The Lake Forest Park Water District (District) is a special purpose district that owns and operates a water system located in the north central part of King County. Origins of the current community water system began with real estate developments by Ole Hanson & Co. in 1910. The Lake Forest Park Water Company, a privately owned water utility, was established in 1926. The utility was purchased by its customers for $50,000 from Lake Forest Park Water Company in 1948. On June 19, 2000 the District formally changed its name from “King County Water District #83” to “Lake Forest Park Water District”. From a physical standpoint, the District has changed significantly over the past several years with the addition of the Horizon View wellfield and the Seattle Public Utilities-Tolt intertie on 195th Street along with other distribution infrastructure changes. The District’s retail service area is made up of 1.5 square miles located wholly within the city of Lake Forest Park within King County. The District serves 2,233 of the City of Lake Forest Park’s 13,091 residents. Approximately 98 percent of the use is residential, with 873 of the total 889 connections providing water to Single Family Residences in 2014, and eleven commercial connections. The District lies at the north end of Lake Washington and is bordered on the north and east by the Northshore Utility District (NUD) and on the south and west by the North City Water District (NCWD). The District owns and operates a Group A water distribution and storage system. The topography of the District’s service area has historically required four pressure zones, High, Intermediate, Low, and Beach in order to keep service pressures in a reasonable range. A new pressure zone has recently been created by the Horizon View reservoir. Water supply for the District is produced from its six wells in two wellfields, which draw from the same aquifer. Emergency interties with neighboring utilities have been put in place for use as needed. The District does not purchase water at this time, instead relying on groundwater sources. According to 2014 estimates, 90 accounts inside the service area for the District were served by neighboring utilities. The District believes a source meter problem contributed to high unaccounted water loss reported in the distribution system, and is reevaluating metering. The District reports, on average between 2010 and 2014, 208 million gallons metered annual water consumption, 0.57 million gallons per day (mgd), with a peak day of production at 0.63 mgd. The 2014 average daily consumption per residential customer was 185.7 gallons. The District’s Capital Improvement Plan recommends improvements totaling approximately $7.4 million over a twenty-year period. Approximately $2.42 million in improvements is planned over the next six years, and an additional $1.49 million in the following five years, totaling $3.91 million in that eleven-year period. The District’s revenue for operations and capital improvements is covered entirely through charges to customers. The District’s capital improvement program has insufficient funding based on its current rate structure. A utility rate consultant was engaged in 2014 to carry out a revenue requirements and rate structure review. The District plans to raise the Capital Improvement Fund rate and seek additional debt financing to cover near-term capital improvements. Reclaimed Water The District completed King County’s Water Reclamation Evaluation Checklist. SEPA The District completed a State Environmental Policy Act (SEPA) checklist for the Plan and, as lead agency under SEPA, issued a determination of nonsignificance for the approval of the Plan on September 8, 2016. There were no appeals. |
|  | A. General, water and sewer plan specific King County Code (KCC) 13.24.010 | Comments/findings |
| (1) | RCW 57.16.010 requires that general comprehensive plans by special purpose districts be submitted to, and approved by, the legislative authority within whose boundaries all or a portion of a utility lies. The King County Code is applicable to water utilities that obtain or distribute water in unincorporated areas of King County. | The District is authorized under chapter 57.16 RCW and so review and approval of the plan by Council is required by statute. The District does not distribute water in unincorporated areas of King County. |
| (2) | Water system plans should be submitted every six years or sooner if required by the Washington State Department of Health (DOH). | The District’s last water plan was submitted in 2006. The District submitted the Plan to the DOH in 2016 and will seek approval of the Plan. |
| (3) | The infrastructure for existing and future service areas based on adopted land use map. | Not applicable as the District does not serve unincorporated King County. |
| (4) | The Plan contains sufficient information to demonstrate the ability to provide services consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes, the Plan demonstrates that the District has ample water supply to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. |
| (5) | The Plan is consistent with Washington Administrative Code (WAC) 246-290-100 for the water service. | Yes, the Plan is consistent with the applicable rules. |
|  | B. Consistency requirements: 13.24.060 |  |
| (6) | King County Code related to the installation of fire hydrants and water mains. | Yes, the Plan proposes to provide adequate fire flow for the urban areas, including capital improvements to construct redundant looping to improve fire capacity. The District also holds a 50 year agreement with Seattle Public Utilities for emergency water supply that includes fire protection. |
| (7) | State and local health requirements. | The Plan has not yet been approved by DOH. The UTRC review process included a representative of Public Health-Seattle and King County. |
| (8) | Elimination or prevention of duplicate facilities. | The District has written agreements with other water providers regarding areas to be served in order to avoid overlapping jurisdiction and to ensure efficiency in the use of existing facilities. |
| (9) | Promotion of most healthful and reliable services to the public. | Yes. The District’s Plan addresses water quality concerns and corrective actions, including for coliform bacteria detected in the distribution system on average once per year since 2006. Measures are indicated that address continued testing, annual line flushing, facility improvements, disinfection of distribution reservoirs, and improvements to monitoring to improve water quality. The District does not chlorinate or fluoridate water supply but maintains standby disinfection capacity for emergency bacterial events. |
| (10) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Currently, the District charges a rate that is in the affordable range. |
|  | C. King County Comprehensive Plan (KCCP) – consistency with provisions and specific policies |  |
| (11) | Consistency with the KCCP and applicable County plans and policies including the Flood Hazard Management Plan and Emergency Response Plan. | Yes, the Plan is consistent with the applicable comprehensive plans and policies. |
| (12) | Consistency with the Coordinated Water System Plans adopted in KCC 13.28. | Yes, the Plan is consistent with the East King County Coordinated Water System Plan. The District does not expect to expand its service area. |
| (13) | Basin-wide or multi-basin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology or the Washington State Department of Health. | The District acknowledges salmon recovery priorities and the relevance of Endangered Species Act listings. |
| (14) | Applicable state water quality, water conservation (e.g., chapter 90.54 RCW and RCW 90.48.495), and waste management standards. | The District’s water use efficiency forms report a high water loss the past few years, and the District believes there is a source meter problem. The District is currently reevaluating water loss to determine if it is above the 10 percent State standard. If the District has water loss above 10 percent, it will complete a water loss control plan. |
| (15) | Growth Management Act; chapter 36.70A RCW. | Yes, the Plan is consistent with the Growth Management Act. See specific policies below. |
| (16) | Groundwater Management Plans. | Not applicable. The District will submit its Wellhead Protection Program to the City of Lake Forest Park for use in its critical areas ordinance. |
| (17) | Federally-approved habitat conservation plans and recovery plans under Endangered Species Act, and other plans, including regional water supply or water resource management plans. | The District identifies that Puget Sound Chinook and possible Bull Trout populations live in McAleer and Lyons Creeks. The District will implement construction prohibitions if salmon watcher sites identify salmon presence in these streams. There is no applicable regional water supply plan. |
| (18) | Applicable requirements to evaluate opportunities for the use of reclaimed water under chapter 90.46 RCW. | Yes, the District evaluated reclaimed water use opportunities. |
| (19) | State Environmental Policy Act documentation. | The District completed a SEPA checklist and issued a determination of nonsignificance for approval of the plan on September 8, 2016, with no appeals. |
|  | COUNTYWIDE PLANNING POLICIES |  |
| (20) | DP‐13: All jurisdictions shall plan to accommodate housing and employment targets. This includes: “Coordinating water, sewer, transportation and other infrastructure plans and investments among agencies, including special purpose districts;…”. | Yes, the District does this in coordination with neighboring jurisdictions. See 23. |
| (21) | PF‐4: Develop plans for long‐term water provision to support growth and to address the potential impacts of climate change on regional water resources. | The District states water supply will support anticipated growth. The Plan does not discuss climate change impacts on water supply. |
| (22) | PF‐5: Support efforts to ensure that all consumers have access to a safe, reliably maintained, and sustainable drinking water source that meets present and future needs. | Yes, the District does this. |
| (23) | PF‐6: Coordinate water supply among local jurisdictions, tribal governments, and water purveyors to provide reliable and cost‐effective sources of water for all users, including residents, businesses, fire districts, and aquatic species. | The District has emergency agreements in place with the North City Water District and the Northshore Utility District. The District does not have service area agreements for residents within the district served by North City Water District or Northshore Utility District. The District is in discussions with neighboring Districts regarding feasibility of combining utilities. Such considerations of merger are not part of this comprehensive plan. |
| (24) | PF‐7: Plan and locate water systems in the Rural Area that are appropriate for rural uses and densities and do not increase the development potential of the Rural Area. | Not applicable. |
| (25) | PF‐8: Recognize and support agreements with water purveyors in adjacent cities and counties to promote effective conveyance of water supplies and to secure adequate supplies for emergencies. | The District has agreements with neighboring utilities for emergency response. The District has emergency interties with Seattle Public Utilities (50 year agreement) and the Northshore Utility District (interlocal agreement). The District has mutual aid agreements with both the Northshore Utility District and the North City Water District to provide staffing and equipment support in the event of an emergency. |
| (26) | PF‐9: Implement water conservation and efficiency efforts to protect natural resources, reduce environmental impacts, and support a sustainable long‐term water supply to serve the growing population. | See 14. |
| (27) | PF‐10: Encourage water reuse and reclamation, especially for high‐volume non‐potable water users such as parks, schools, and golf courses. | See 18. The District completed King County’s Water Reclamation Evaluation Checklist. |
|  | KING COUNTY COMPREHENSIVE PLAN (KCCP) POLICIES |  |
| (28) | F-107: Plan for provision of services to rural areas. | Not applicable. |
| (29) | F-108: King County to work with cities and service providers to establish priority areas for public funding of capital facilities. | The District’s capital improvement program (CIP) has insufficient funding based on its current rate structure. Operating Revenues under current rates are adequate to cover projected operating expenses and provide a small contribution to the capital fund at least for several years. An evaluation of rates is scheduled. |
| (30) | F-201: All facilities and services should be provided in compliance with provisions and requirements of the Endangered Species Act (ESA) and the Clean Water Act. | Yes, to the extent known, facilities and service are provided consistent with the federal laws. |
| (31) | F-209: Support rural levels of development and not facilitate urbanization. | Not applicable. |
| (32) | F-210: Capital facility plans and improvement programs for services to unincorporated King County are consistent with the KCCP. | Not applicable. |
| (33) | F-211: King County helps coordinate development of utility facilities. | Yes, to the extent applicable, King County will do this. |
| (34) | F-221: King County shall initiate a sub-area planning process with any service provider that declares, in its capital facilities plan, an inability to meet service needs within service area. | Not applicable. The District did not identify any inability to meet service needs within its service area. |
| (35) | F-223: If a service deficiency is identified in a service provider's existing service area, King County and the applicable service provider shall remedy the deficiency through a joint planning process addressing capital improvement programs and long-term funding strategies reuse programs. | Not applicable. The District did not identify any inability to meet service needs within its service area. |
| (36) | F-231: King County supports coordination of regional water supply planning, sales of excess water supplies among municipalities in the region, water quality programs and water conservation, reuse and reclaimed water programs. | Yes, the District supports regional water supply coordination. |
| (37) | F-232: Water utilities that obtain water from, or distribute water in unincorporated King County, and water utilities formed as special purpose districts under Title 57 RCW are required to submit water system plans to the County for review and approval and shall describe in their plans how they intend to meet their duty to provide service within their retail service areas. | The District is a special purpose district authorized under Title 57 RCW and so review and approval of the plan by the County is appropriate. The District does not distribute water in unincorporated areas of the county. The District did describe service area policies for its retail service area. |
| (38) | F-248 King County shall partner with utilities to publicize water conservation and encourage best management practices that conserve potable water supply through measures that include use of alternative supplies such as reclaimed water. | Yes, the County will do this. |
| (39) | F-246: King County supports interties that allow the transfer of water resources among water utilities to meet the projected demands for growth where such interties meet the requirements of RCW 90.03.383 and are also consistent with any applicable locally adopted comprehensive plans, regional water supply plans, adopted groundwater management plans, watershed plans, approved Coordinated Water System Plans, and response requirements of ESA and Clean Water Act. | The Plan is consistent with the East King County Coordinated Water System Plan. |
| (40) | F-249: Utilities with more than one thousand service connections required to submit water system plans for approval to King County shall include an evaluation of reclaimed water use opportunities by completing King County’s Water Reclamation Evaluation. | The District did an evaluation of reclaimed water use; use of reclaimed water is not in this Plan. |
| (41) | F-251: In its review of water system plans, the UTRC shall consider the criteria provided in KCC 13.24.010, 13.24.060, and 13.24.070, and determine the plan’s consistency with the following: a. Applicable provisions of the King County Comprehensive Plan, land use plans, and development regulations adopted under the Growth Management Act; b. Approved or adopted regional water resource plans, such as basin plans, groundwater plans, watershed-based conservation and recovery plans developed under ESA, salmon recovery plans developed under chapter 77.85 RCW, water resource plans developed under chapter 90.54 RCW, watershed plans developed under chapter 90.82 RCW, and a regional water supply plan or water resource management plan; c. The County’s Regional Wastewater Services Plan; and d. Other applicable provisions of countywide plans managed by King County, as specified in UTRC Guidance or checklists. | The UTRC did consider these issues and recommends approval of the Plan. |
| (42) | F-252: In reviewing proposals for modified and expanded service area boundaries for municipal water suppliers, the UTRC shall consider, in addition to Policy F-251: a. Compliance by the water system with its water system comprehensive plan, including water conservation elements; b. Whether it can meet its duty to provide service within its service area, as required under chapter 43.20 RCW; and c. Consistency with the service provisions of any applicable Coordinated Water System Plan, as adopted in King County Code Chapter 13.28. | The District is not planning to change its service area boundaries. The District has a capital improvement plan and growth projections that consider and confirm adequate supply in the possibility of boundary re-districting such as could happen if the North City Water District was annexed by Shoreline and the City of Lake Forest Park were to annex the District. |
| (43) | F-253: Consistent with Countywide Planning Policies, public drinking water system surface water reservoirs and their watersheds should be managed primarily for the protection of drinking water, but should allow for multiple uses, including recreation, when such uses do not jeopardize drinking water quality standards. Public watersheds must be managed to protect downstream fish and agriculture resources. | The District limits public access in the source watershed. Protections include fencing, security cameras, chemical-free ground maintenance, and restrictions to above ground structures and trees within 10 feet of the of the reservoir boundary. The District will develop further watershed protection plans in response to local interest in creating a walking trail along McKinnon Creek through the watershed. The District initiated a Quiet Title action with the City of Lake Forest Park to clarify ownership of certain properties in the watershed. The District conducted community education efforts in 2014 and 2015, and a wellhead protection and communications advisory committee was established. |
| (44) | F-254: Groundwater-based public water supplies should be protected by preventing land uses that may adversely affect groundwater quality or quantity to the extent that the supply might be jeopardized. The County shall protect the quality and quantity of groundwater used as water supplies through implementation of Policies E-493 through E-497 where applicable. | The District’s Wellhead Protection Program will be submitted to the City of Lake Forest Park. |