2020 Preliminary Vashon Rural Town Affordable Housing 
Special District Overlay Evaluation

December 2020

Contents

II.	Executive Summary	3

III.	Background	4

IV.	Report Requirements	7

A.	Assess the efficacy of its scope and standards in achieving the Overlay's purpose of incentivizing affordable housing within the Vashon Rural Town	7

B.	Recommendations to retain, amend or repeal the Special District Overlay	7

C.	Examination of the advantages and disadvantages of the Special District Overlay	7

D.	A review of the relationship between the parcels that the Special District Overlay applies to and potable water supply	9

E.	The public benefits and risks of retaining or repealing the Special District Overlay	9

F.	The current need for affordable housing on Vashon-Maury Island, including for households with incomes at or below 30 percent of Area Median Income	10

G.	Infrastructure capacity, including public roads and sewer	11

H.	Potential impacts to affordable housing funding if the Special District Overlay is modified or eliminated	11

I.	Ongoing permit applications using the Special District Overlay and feedback from those permit applicants on the efficacy of the Special District Overlay	12

J.	Evaluation of whether any code changes are necessary to fulfill the purpose of the Special District Overlay	12

V.	Conclusion/Next Steps	13

VI.	Appendices	15

# Executive Summary

The Vashon-Maury Island Community Service Area Subarea Plan (CSA Plan) was adopted by the King County Council in December 2017. The CSA Plan includes long-range policies and strategies to achieve the community’s vision for Vashon-Maury Island. The development of the CSA Plan included a wide-reaching community engagement program, a result of which was the prioritization of increasing the amount and availability of housing in the Vashon Rural Town that is affordable to low-income residents. To address this priority, the CSA Plan includes the Vashon Rural Town Affordable Housing Special District Overlay (Overlay), a voluntary incentive program meant to spur the creation of affordable housing within the Vashon Rural Town, the mixed-use center of Vashon-Maury Island that contains the highest density of housing, commercial, and industrial land uses on the Island.

This Report is the third annual evaluation of the effectiveness of the Overlay required by Ordinance 18623. In analyzing the relationship between properties covered by the Overlay to potable water supply, public road and sewer capacity, potential impacts to affordable housing funding, the need for housing affordable for low-income households on Vashon-Maury Island, and ongoing permit applications that propose to use the Overlay to construct affordable housing, this Report finds distinct advantages and disadvantages to the Overlay. Advantages of the Overlay include its focus on the highest level of housing need in the community (affordable at 60 percent of area median income) and its location in the Vashon Rural Town, which has the Island’s highest density of employment opportunities, transit routes, and other services that support and complement higher-density residential buildings. Identified disadvantages include the focus on development with exclusively affordable housing as opposed to mixed-income developments and the Overlay’s similarities to King County’s Residential Density Incentive program, which has not been utilized on the Island.

Weighing these factors, this report concludes that although no new affordable housing units have been constructed utilizing the Overlay at this time, there is insufficient data to affirmatively conclude whether this is a result of the content of the Overlay, if it is due to external factors, or some combination thereof. The existence of an active application proposing to utilize the Overlay indicates that it is a sufficient incentive to construct affordable housing in the Vashon Rural Town that would not otherwise be feasible. Therefore, the report recommends no changes to the Overlay at this time.

# Background

Department Overview: The Department of Local Services provides infrastructure and land use planning services to the residents of rural and urban unincorporated King County. The Permitting Division of the Department of Local Services processes, reviews, and issues land use and building permits for unincorporated areas of King County, including Vashon-Maury Island. Any land use application that utilizes the Vashon Rural Town Affordable Housing Special District Overlay would be processed and reviewed by the Permitting Division.

Key Historical Context: In December 2017, the King County Council adopted the Vashon-Maury Island Community Service Area Subarea Plan (CSA Plan) via Ordinance 18623. The CSA Plan includes long-range strategies informed and defined by the Island’s unique aspirations and values to achieve the community’s vision. The CSA Plan, which is an element of the King County Comprehensive Plan, was developed with substantial public engagement and includes Island-specific policies, strategies, and action items addressing a broad range of topic areas such as land use, housing, parks, and transportation.

A central theme that emerged throughout the extensive public engagement effort associated with the CSA Plan in 2016 and 2017 was a desire to “increase the amount of housing in Vashon Rural Town that is affordable to low-income residents.” There is broad consensus among Puget Sound housing experts that the region is experiencing a housing affordability crisis that also affects Vashon-Maury Island.

To address this priority, the CSA Plan includes the Vashon Rural Town Affordable Housing Special District Overlay (Overlay), a voluntary incentive program meant to spur the creation of affordable housing within the Vashon Rural Town, the mixed-use center of Vashon-Maury Island that contains the highest density of housing, commercial, and industrial land uses on the Island. The Overlay offers density bonuses – the ability to build one and a half to four times the number of housing units that would be allowed under existing zoning, depending on the zone – in exchange for the provision of housing units affordable for households with incomes at or below 60 percent (for at least half of the units) and 80 percent (for the remainder of the units) of the Area Median Income (AMI), as well as the installation of several water conservation features.

Ordinance 18623, which adopted the Overlay, requires transmittal to the Council of an annual series of written evaluations assessing the efficacy of the scope and standards of the Overlay in incentivizing the development of affordable housing within the Vashon Rural Town. This Report is the third and final annual report required by Ordinance 18623 and examines the advantages and disadvantages of the Overlay and its relationship to potable water supply, public roads, and sewer, as well as an evaluation of whether any King County Code changes are necessary to fulfill the Overlay’s purpose. Ordinance 18623 requires that a draft final evaluation of the Overlay be completed within 90 days of either issuance of the first permit necessary to result in 120 units of housing created through the Overlay or four years after the effective date of the Ordinance 18623 (December 24, 2021), which would be March 24, 2022, whichever occurs first. In addition, the draft final evaluation will be posted for a minimum 45-day public comment period; a final report must be transmitted to the Council within 60 days of the end of the public comment period.

Key Current Context: The Overlay was adopted in December 2017 as a component of the CSA Plan. As stated in King County Code (K.C.C.) 21A.38.270, the purpose of the Overlay is to incentivize the creation of affordable housing on certain parcels in the Vashon Rural Town in exchange for the opportunity to build more housing units than would be allowed under existing zoning, a land use strategy known as a “density bonus.” The Vashon-Maury Island Community Advisory Group, which served in an advisory capacity during the development of the CSA Plan, indicated a preference for this approach over other affordable housing tools such as inclusionary zoning, which requires that a certain percentage of units in new residential developments be reserved for income-qualified households. The Advisory Group also expressed a desire to require affordable housing be built to a higher environmental standard than other housing.

Per K.C.C. 21A.38.270, any residential or mixed-use development on parcels in the Overlay that complies with the following key standards is eligible for the Overlay’s density bonuses:

- At least 50 percent of units affordable at or below 60 percent AMI, with the remainder affordable at or below 80 percent AMI.

- Rates for rental units, including the average cost of essential utilities, set at or less than 30 percent of maximum gross income at each income level.  Sale prices for owner-occupied units set at affordable rates based on income level.

- Affordable rental housing units will remain affordable for a minimum of 30 years. Affordable owner-occupied housing units will remain affordable for a minimum of 50 years.

- Incorporation of at least three water conservation measures, including one outdoor measure.

- Connection to public water and sewer.

The Overlay includes parcels that are zoned R-1, R-4, R-8, R-12, and Community Business. The following table summarizes the maximum density available through the Overlay in each zone.

| Zone | Existing Allowed Density | Maximum Density under Special District Overlay |
| --- | --- | --- |
| R-1 | One dwelling unit per acre | Four dwelling units per acre |
| R-4 | Four dwelling units per acre | Eight dwelling units per acre |
| R-8 | Eight dwelling units per acre | 18 dwelling units per acre |
| R-12 | 12 dwelling units per acre | 18 dwelling units per acre |
| Community Business | Mixed-use only; maximum density of eight dwelling units per acre under development condition VS-P29 | 18 dwelling units per acre |

The Overlay requires compliance with more stringent criteria, including the level of affordability and environmental features, than King County’s existing Residential Density Incentive Program (K.C.C. Chapter 21A.34), which also provides density bonuses and additional units in exchange for the provision of different types of affordable housing, among other items.

Report Methodology:  This report was produced by Department of Local Services – Permitting Division staff and input from staff from the Housing, Homelessness and Community Development Division of the King County Department of Department of Community and Human Services. Data on existing permits was gathered from the Permitting Division’s Accela permit database, with additional information about housing affordability from the U.S. Department of Housing and Urban Development’s data sets.

# Report Requirements

This section is organized to align with the requirements for this Report outlined in Ordinance 18623, Section 10.

## Assess the efficacy of its scope and standards in achieving the Overlay's purpose of incentivizing affordable housing within the Vashon Rural Town

The development of income-restricted affordable housing units, regardless of whether density bonus or other incentive programs are utilized, often requires the coordination of multiple funding sources and the fulfillment of administrative requirements that can take years to come together; a typical project takes at least two to three years from conception to completion.

The Overlay has not been used to create new affordable housing units in the Rural Town since its adoption in December 2017. At this time, it is not possible to determine whether this is due to the efficacy of the scope and standards of the Overlay or external factors due to the length of time it takes to develop affordable housing units, as noted above.

The 2019 filing of a pre-application request for a 41-unit affordable housing project utilizing the Overlay suggests that at least one affordable housing developer considered the Overlay as a possible feasible means to create affordable housing units.

## Recommendations to retain, amend or repeal the Special District Overlay

Because there is insufficient data to conclude that the lack of affordable housing development utilizing the Overlay is due to the Overlay itself as opposed to larger market forces, this report recommends that the Vashon Rural Town Affordable Housing Overlay be retained without amendment. Similarly, modifying or repealing the Overlay at this time would be premature given the length of time to develop affordable housing. Keeping the Overlay in place will allow for continued consultation with interested developers and to better understand the strengths and weaknesses of the incentives and requirements. Additional time would also enable better points of comparison with other development trends on Vashon-Maury Island and the Vashon Rural Town to inform whether the Overlay’s incentives are effectively calibrated to achieve its purpose.

## Examination of the advantages and disadvantages of the Special District Overlay

Analysis of Overlay identified the following advantages and disadvantages.

Advantages

- The Overlay applies to parcels identified based on their potential for development or redevelopment for new housing. This ensures that developers interested in creating affordable housing will be directed to parcels where new development is likely to be successful.

- The bonus density with the Overlay is proportionate to each parcel’s base zoning. This will ensure that the scale of future development that utilizes the bonus density in the Overlay will be proportional to the CSA Plan’s land use vision for the Rural Town.

- The Overlay focuses on the highest level of need in the community, at or below 60 percent of AMI.

- All Overlay parcels are within the Vashon Rural Town, which is the focus area for all new multifamily residential development on the Island as directed by the CSA Plan. The Vashon Rural Town has the Island’s highest density of employment opportunities, transit routes, and other services that support and complement higher-density residential buildings.

Disadvantages

- The Overlay is applicable only to developments that consist entirely of affordable units; this precludes the construction of affordable units in buildings with a mix of market-rate and affordable units from taking advantage of the density bonus.

- The Overlay has a structure similar to the Residential Density Incentive Program but requires compliance with more stringent requirements to qualify for bonuses that provide less additional density. To date, the Residential Density Incentive Program has not been utilized on Vashon-Maury Island, indicating that a more burdensome program such as the Overlay may be even less feasible.

- Higher allowed densities and the ability to build more units than would otherwise be allowed are the primary incentive offered by the Overlay to developers in exchange for the provision of affordable housing units. However, while those higher densities are available in theory, Water District 19, which serves the Vashon Rural Town, has an ongoing moratorium on new water “shares,” and limited existing water connections will make it difficult to realize density bonuses in practice because a developer will only be able to construct as many new housing units as they have water shares, regardless of how many they are permitted to build through the Code.

- The required water and energy efficiency measures of the Overlay (K.C.C. 21A.38.270.C.2) may increase up-front construction costs and may be seen as a disincentive to development.

- The Overlay references specific rates of water usage in its required water conservation features – for example, “install all bathroom faucets with 1.5 gallons per minute or better,” and “install all kitchen faucets not to exceed two gallons per minute.” In the future, more water-efficient features may be available, and the requirements included in the Overlay may represent suboptimal levels of water conservation technology, undercutting the water conservation benefit of the Overlay.

## A review of the relationship between the parcels that the Special District Overlay applies to and potable water supply

The Overlay is entirely located within Water District 19’s local service area. The majority of the 246 parcels to which the Overlay applies are within 200 feet of an existing water main. However, this does not ensure automatic approval of a domestic water supply service; a development will be able to construct only as many units as the number of water units allocated to the parcel allows, regardless of the potential density under the Overlay. Water District 19 will issue a Certificate of Water Availability after a determination of serviceability is completed for an individual parcel.

## The public benefits and risks of retaining or repealing the Special District Overlay

Analysis of Overlay identified the following public benefits and risks of its retention or repeal.

Public Benefits of Retaining the Special District Overlay

The primary public benefit of retaining the Overlay is that it provides an incentive to build new affordable housing developments that would otherwise not be feasible. Taking the opportunity to work with developers interested in utilizing the Overlay will provide the County with better indicators of its strengths and opportunities. Leaving the Overlay in place would provide the County with better data to support a future decision to retain, modify, or repeal it.

Public Risks of Retaining the Special District Overlay

This report identifies no significant risks in retaining the Overlay. Historic low levels of building permit activity in Vashon Rural Town, coupled with Water District 19’s ongoing moratorium on new potable water connections, are expected to decrease the risk of unmanageable growth. Some risk exists that a developer who has an interest in building affordable housing units in the Vashon Rural Town may deem the Overlay requirements too stringent, and choose to invest elsewhere. However, a developer may still build affordable housing within Vashon Rural Town under the density allowed by the base zoning without the using the Overlay.

Public Benefits of Repealing the Special District Overlay

The Overlay is a voluntary incentive, which means that any parcel to which it applies can be developed in compliance with normal development regulations. In other words, the presence of the Overlay does not diminish the development potential of any parcel compared to its value prior to the Overlay’s adoption. Therefore, there appears to be no clear public benefit to repealing the Overlay.

Public Risks of Repealing the Special District Overlay

Repealing the Overlay would present a risk to the public if the feasibility of a proposed affordable housing development in the Rural Town is dependent on the bonus densities provided by the Overlay, and the Overlay is repealed prior to that project vesting to existing development regulations. Given the length of the permit review process, it is likely that the Permitting Division would be aware of such a project during the time that a legislative process to repeal of the Overlay would take place. Because there is one proposed project that has completed a pre-application process but has not vested to existing development regulations that could be impacted in the case that the Overlay is repealed, there is limited immediate public risk associated with repealing the Overlay.

## The current need for affordable housing on Vashon-Maury Island, including for households with incomes at or below 30 percent of Area Median Income

U.S. Department of Housing and Urban Development Comprehensive Housing Affordability Strategy data from 2018 indicate that approximately 12 percent of households on Vashon-Maury Island have an income at or below 30 percent of AMI, including 38 percent of renter households.

In 2017, an estimated 24 percent of Vashon-Maury Island residents experienced a housing cost burden (paying more than 30 percent of income for housing costs), including 51 percent of renters and 69 percent of renters with a household income at or below 30 percent AMI. As of September 2020, Vashon Household, a local affordable housing developer and manager, had 50 seniors on a waitlist for its senior living apartments and 65 on the homeless and general population (non-senior or homeless) waitlist.

Compounding the lack of rent-restricted housing is the overall paucity of rental housing on Vashon-Maury Island, as only 20 percent of the total number of housing units on Vashon are renter-occupied, compared with 43 percent across King County as a whole. The lack of rental housing leaves renters with few housing options. Nearly 90 percent of housing units on the Island are one-unit detached structures, and just over seven percent of units are in a multifamily building.

## Infrastructure capacity, including public roads and sewer

Vashon Island’s road system is entirely rural. It is characterized by low traffic volumes and congestion levels, with occasional spikes in traffic occurring during island festivals and when scheduled inbound ferry traffic arrives. There is currently no active traffic volume monitoring on Vashon-Maury Island because traffic volumes remain low relative to road capacities and intersection levels of service standards. All new development proposals within unincorporated King County are assessed according to the King County Transportation Concurrency Management Program to ensure that sufficient public facilities are in place to carry the traffic associated with a proposed development. Because traffic volumes are generally low on the Island, adverse impacts on transportation infrastructure caused by future development utilizing the Overlay are not expected.

According to King County’s Wastewater Treatment Division, the Vashon Treatment Plant treats approximately 180,000 gallons of wastewater per day with a maximum design capacity of 1.4 million gallons of wastewater per day during peak storms. Vashon Sewer District, which operates the sewage collection system in the Vashon Rural Town that discharges to the County’s Vashon Treatment Plan, has approximately 460 existing connections to their sewer system. In 2020, new connections to sewer in the County’s regional sewer system pay a capacity charge fee of $66.35 per residential customer equivalent per month for 15 years to the County in addition to a monthly sewer fee and any charges from the local sewer agency. This fee is billed to the property owner. Adding new connections that are offered through the Overlay could increase the current customer base and service demands on the District’s infrastructure, but there is no identified concern that the Overlay will create an undue burden on the system. Per King County Code, new rent-restricted housing in multifamily structures in which at least 51 percent of units are affordable at 80 percent of AMI with affordability protections for at least 40 years are eligible for a capacity charge discount of 50 percent in most cases. This factor could reduce barriers to the construction of affordable housing for developments that meet these criteria.

## Potential impacts to affordable housing funding if the Special District Overlay is modified or eliminated

By incentivizing the construction of affordable housing, the Overlay increases the potential pool of applicants for existing sources of public funding of affordable housing developments. Modifications that would make the Overlay more attractive to developers, such as by reducing the number of units that are required to be affordable or increasing the density bonus, could potentially increase competition for existing sources of affordable housing funding. Conversely, making the Overlay less attractive by deepening the affordability levels of the housing units, could have the decrease the completion for housing funding on Vashon-Maury Island. Eliminating the Overlay altogether could reduce the competition for existing affordable housing funding for Vashon-Maury Island.

## Ongoing permit applications using the Special District Overlay and feedback from those permit applicants on the efficacy of the Special District Overlay

The following data summarize the inquiries, applications, and permits related to the Overlay that the Permitting Division has processed between the adoption of the Overlay in December 2017 and October 2020.

  - Overlay application inquiries at Permitting Division (e.g. phone calls or e-mails asking for information about the ordinance since its approval in 2017): One walk-in customer.

  - Overlay-related applications filed (e.g. pre-application meeting, subdivision, critical area, building permit applications, fees): One pre-application meeting was completed on August 29, 2019 (PREA19-0139).  Applicants proposed utilizing the Overlay to construct a 41-dwelling unit workforce housing development on parcel 2923039148, zoned R-4 and subject to VS-P31, a development condition restricting use of the property to low-income housing., Applicant has not submitted further applications.

  - Overlay-related permits issued by Permitting Division:  None.

Because no permit applications have been submitted, no feedback on the efficacy of the Overlay from permit applicants is available.

## Evaluation of whether any code changes are necessary to fulfill the purpose of the Special District Overlay

Per K.C.C. 21A.38.270, the purpose of the Overlay is “to provide an optional incentive that will lead to an increase in the supply of affordable housing within the Vashon Rural Town.” In the three years that it has been available, the Overlay has not been used to create new affordable housing units in the Rural Town. However, there is insufficient data to conclude that the lack of affordable housing development utilizing the Overlay is due to the Overlay itself as opposed to larger market forces. Leaving the Overlay in place will allow for continued consultation with potential interested developers and offer the County the opportunity to better understand the strengths and challenges of its incentives and requirements. Additional time would also provide clearer points of comparison with other development trends on Vashon-Maury Island and the Vashon Rural Town to determine whether the Overlay’s incentives are effectively calibrated to achieve its purpose.

It cannot currently be determined whether the paucity of Overlay-related permit activity is due to the Overlay’s weaknesses or to underlying market conditions. The filing of a pre-application request to discuss a 41-unit affordable housing project utilizing the Overlay suggests that at least one affordable housing developer potentially considered the Overlay to be workable. No code changes are recommended at this time to fulfill the purpose of the Overlay.

# Conclusion/Next Steps

During the community engagement process for the Vashon-Maury Island Community Service Area Subarea Plan, increasing the amount of housing in Vashon Rural Town that is affordable to low-income residents was identified as a key priority. Adopted in December 2017 as part of the CSA Plan, the Vashon Rural Town Affordable Housing Overlay was created to incentivize the development of housing for low-income residents of Vashon-Maury Island through density bonuses – the ability to build more units than would be allowed under existing zoning. Although no permits for affordable housing utilizing the Overlay have been issued at the time of this report, there is not data to suggest that this is due to any particular regulation included in the Overlay. For this reason, no changes to the Overlay are recommended at this time.

Pursuant to Ordinance 18623, Section 10, a draft evaluation of the Overlay must be completed within 90 days of either the issuance of the first permit that would result in 120 units of affordable housing created through the overlay or four years after the effective date of the ordinance (December 24, 2021), which would be March 24, 2022. A minimum 45-day public comment period on that draft evaluation is also required, followed by a final evaluation report to be transmitted to the Council within 60 days of the end of the comment period. This final evaluation represents an opportunity for further analysis of the effectiveness of the Overlay with the benefit of additional data points, time to receive feedback from applicants as they navigate the permit process, and public input through the comment period. Additionally, other ongoing affordable housing-related work at King County may inform the final evaluation of and potential modifications to the Overlay. This includes the work of the Affordable Housing Committee of the Growth Management Planning Council, which is beginning implementation of its Five-Year Action Plan to “eliminate cost burden for households earning 80% Area Median Income and below, with a priority for serving households at or below 50% Area Median Income.” Also applicable will be the outcomes of the Vashon-Maury Island alternative housing demonstration project currently in development, the purpose of which is to “test development regulations for alternative housing models” to “provide opportunities for lower rent housing options.”, The goals of the Five-Year Action Plan and the alternative housing demonstration overlap with the goal of the Overlay. As these efforts consider and solicit feedback from stakeholders about similar regulatory approaches to increasing the supply of affordable housing in the high-cost King County area, the Permitting Division will be tracking this work for possible application to the Overlay.

# Appendices

Appendix A – Ordinance 18623, Section 10

A. A written evaluation of the special district overlay, as adopted in section 9 of this ordinance, shall be conducted by the executive to assess the efficacy of its scope and standards in achieving the overlay's purpose of incentivizing affordable housing within the Vashon Rural Town, and shall include recommendations to retain, amend or repeal the special district overlay.  The evaluation shall examine the advantages and disadvantages of the special district overlay, including a review of the relationship between the parcels that the special district overlay applies to and potable water supply.  Other factors the evaluation shall consider include, but are not limited to: the public benefits and risks of retaining or repealing the special district overlay; the current need for affordable housing on Vashon-Maury Island, including for households with incomes at or below thirty percent of area median income; infrastructure capacity, including public roads and sewer; and potential impacts to affordable housing funding if the special district overlay is modified or eliminated.

B. The evaluation shall include annual reports and a final report:

1. The executive shall conduct preliminary evaluations that include the information in subsection A. of this section, as well as the following information:

a. a list and evaluation of ongoing permit applications using the special district overlay, and feedback from those permit applicants on the efficacy of the special district overlay;

b. evaluation of whether any code changes are necessary to fulfill the purpose of the special district overlay; and

c. for the first annual report and the final report, information of other jurisdictions approaches to incentivizing development of affordable housing, and evaluation of whether those approaches would be appropriate to Vashon-Maury Island.

d. The executive shall file three preliminary evaluation reports, and either a motion accepting each report or an ordinance proposing necessary code changes to further the purposes of the special district overlay.  These reports shall be filed annually no later than December 31, 2018, December 31, 2019, and December 31, 2020, in the form of a paper original and an electronic copy with the clerk of the council, who shall retain the original and provide an electronic copy to all councilmembers, the council chief of staff, the policy staff director and the lead staff for the transportation, economy and environment committee, or its successor. When the trigger for a final evaluation under subsection 8.2.a. occurs, any subsequent annual reports shall not be required; and

2. A draft final evaluation shall be completed within ninety days of the occurrence of one the following, whichever comes first:

a. issuance of the first permit necessary for construction that would result in a cumulative total of one hundred twenty affordable housing units within the special district overlay; or

b. four years after the effective date of this ordinance.

C. The department shall produce a draft final evaluation including the information required in this section.

D. The department shall include a public comment period for the department's draft evaluation described in subsection A. of this section.  The public comment period shall be at least forty-five days from the date of publication in the Vashon-Maury Island newspaper of record.  As part of this public comment period, the department shall:

1. Publish notice of the draft evaluation's availability in the Vashon-Maury Island newspaper of record that includes locations where the draft evaluation is available;

2. Request comments of the King County water district 19 and the Vashon sewer district;

3. Request comments from any developer that has applied for approval under the special district overlay provisions;

4. Provide a copy at the local library;

5. Provide an electronic copy on the department's website; and

6. Send electronic notice to the clerk of the council, who shall retain the original email and provide an electronic copy to all councilmembers, the council chief of staff the policy staff director and the lead staff for the transportation, economy and environment committee, or its successor.

E. After the public comment period has ended, the department shall prepare a final evaluation of the special district overlay, incorporating or responding to the comments received.  Within sixty days of the end of the end of the public comment period, the executive shall file a final evaluation report, a motion accepting the report, and an ordinance that implements any proposed changes to the special district overlay, in the form of a paper original and an electronic copy with the clerk of the council, who shall retain the original and provide an electronic copy to all councilmembers, the council chief of staff, the policy staff director and the lead staff for the transportation, economy and environment committee, or its successor.

Appendix B – K.C.C. 21A.38.270 - Vashon Rural Town Affordable Housing Special District Overlay

A.  The purpose of the affordable housing special district overlay is to provide an optional incentive that will lead to an increase in the supply of affordable housing within the Vashon Rural Town.  This special district overlay shall only apply on a voluntary basis to the parcels shown in Map Amendment #3 in Attachment B of Ordinance 18623.  Use of the special district overlay is voluntary and these eligible parcels retain all existing development and land use rights and may exercise those without using this special district overlay.

B.  The special district overlay is eligible to be used by any residential or mixed-use development that complies with the following standards:

1.  A minimum of fifty percent of the units in each development shall be affordable to households with incomes at or below sixty percent of area median income, and the remainder of the units in each development shall be affordable to households with incomes up to a maximum of eighty percent of area median income;

2.a.  Rents of rental units, including both rent and the average cost of essential utilities, shall be set at no greater than thirty percent of the maximum gross income for the applicable income level; or

b.  The sales price of owner occupied units shall be set so that they are affordable for income and asset qualified home buyers at the applicable income level.  Prices shall be restricted based on typical underwriting ratios and other lending standards;

3.  The development is located on an eligible parcel as shown in Map Amendment #3 in Attachment B to Ordinance 18623; and

4.  The development adheres to all special district overlay standards listed in subsection C. of this section.

C.  All development shall comply with all applicable King County development regulations, including K.C.C. Title 9, K.C.C. Title 13, K.C.C. Title 14, K.C.C. Title 16, K.C.C. Title 17, K.C.C. Title 19A, K.C.C. Title 20, K.C.C. Title 21A, K.C.C. Title 23, K.C.C. Title 27, and K.C.C. Title 27A, except as follows:

1.  The maximum density shall be as follows:

a.  any parcel zoned R-1 may develop up to a maximum density of four dwelling units per acre;

b.  any parcel zoned R-4 may develop up to a maximum density of eight dwelling units per acre;

c.  any parcel zoned R-8 or R-12 may develop up to a maximum density of eighteen dwelling units per acre;

d.  any mixed use development in the Community Business (CB) zone that contains a residential component may develop up to a maximum density of eighteen dwelling units per acre;

2.  To reduce the impacts of a new development on potable water supplies, the development shall incorporate at least three of the following water conservation measures, and that only one of the outdoor measures from subsection C.3.a. through h. of this section may be counted toward the minimum requirement:

a.  mulch landscape beds with two inches organic mulch;

b.  use grass type requiring less irrigation and minimal maintenance;

c.  use Xeriscape landscape techniques on seventy-five percent or more of site landscaped area;

d.  landscape with plants appropriate for site topography and soil types, emphasizing use of plants with low watering requirements, which means they are drought tolerant;

e. install subsurface or drip systems for irrigation with timers;

f.  install a rainwater collection system, such as a cistern, that reduces water consumption for irrigation by fifty percent annually;

g.  provide one-hundred percent of landscaping water use with captured precipitation or reused water purified without the use of chemicals;

h.  install smart scheduling technology.  This strategy counts for a maximum reduction of thirty percent provided all landscape water use is controlled by a soil moisture sensor control system or a weather-based irrigation control system;

i.  reduce total indoor and outdoor water consumption by at least twenty-five percent over standard practices;

j.  provide water submetering for each unit or entire building where central hot water systems are used;

k.  install all bathroom faucets with 1.5 gallons per minute or better;

l.  install all showerheads not to exceed 1.75 gallons per minute;

m.  install all kitchen faucets not to exceed two gallons per minute;

n.  install high efficiency toilets not to exceed 1.28 gallons per flush or 1.6/1.1 for dual flush;

o.  install no-cartridge waterless urinals or 1/8 gallon urinals and high efficiency toilets as noted above in all common areas; or

p.  install point-source, on-demand or recirculation pump hot water systems, where appropriate;

3.  All new units must connect to public water and public sewer;

4.  Affordable housing units shall remain as affordable housing for a minimum of fifty years for ownership affordable housing units and for a minimum of thirty years for rental affordable housing units, starting from the date of final certificate of occupancy for the development;

5.  Developments shall be landscaped as follows:

a.  when seventy-five percent or more of the units in the development consists of townhouses or apartments, the development shall provide perimeter landscaping and tree retention in accordance with K.C.C. chapter 21A.16 for townhouse or apartment projects;

b.  when less than seventy-five percent of the units in the development consists of townhouses or apartments, the development shall provide landscaping and tree retention in accordance with K.C.C. chapter 21A.16 for townhouses or apartments on the portion or portions of the development containing the units, but if buildings containing the units are more than one hundred feet from the development’s perimeter, the required landscaping may be reduced by fifty percent; and

c.  all other portions of the development shall provide landscaping or retain trees in accordance with K.C.C. chapter 21A.16;

6.  Developments shall provide one off-street parking space per unit.  The director may require additional parking, up to the maximum standards for attached dwelling units, which may be provided in common parking areas.  Off-street parking may be reduced below one per unit, with the approval of the director, with submission of a site-specific parking study that demonstrates that parking demand is met; and

7.  All developments shall provide on-site recreation space at a minimum of fifty percent of the levels required in K.C.C. chapter 21A.14.

D.  Use of the incentive in this section requires an affordable housing covenant recorded against the property as a condition of issuance of any construction permit or recording of a subdivision.

E.  The department is authorized to enforce the requirements of this section, including those pertaining to sale and rental affordability and other requirements of the covenant, through judicial action or administrative action under Title 23.

F.  A preapplication meeting shall be required for developments using the special district overlay in this section.

G.  As part of the preapplication process and before filing an application with the department, the applicant shall hold at least one community meeting in accordance with K.C.C. 20.20.035.  In addition to the requirements of K.C.C. 20.20.035, the applicant shall:

1.  Include in the mailed notice:

a.  the name of the affordable housing developer;

b.  the total number of planned dwelling units;

c.  preliminary architectural renderings of buildings;

d.  preliminary site plan;

e.  the dates, times and locations of community informational meetings about the development;

f.  contact information including names and phone numbers for the developer or applicant; and

g.  a county contact person or agency;

2.  Conduct the meeting or meetings in a location accessible to the public at least thirty days before the anticipated date of application.  The purpose of the meeting is to provide neighboring property owners and residents with information regarding the proposed development and to answer questions regarding the proposed development; and

3.  Prepare and install a four-foot notice board that must be placed in a conspicuous location on the property proposed for development.  The board shall be installed no later than the date the mailed notice for the community meeting is sent and shall remain in place until the development application is abandoned or when the permit is issued.

H.  An application for a development under the special district overlay in this section shall be considered complete when the information required under K.C.C. 20.20.040, as well as the following information and studies have been submitted and are adequate to review the proposal:

1.  A proposed development plan and draft covenant that includes:

a.  the number of dwelling units that are part of the development;

b.  a description of the affordability levels for the units;

c.  the duration of the affordability of the units;

d.  the number of off-street parking spaces, and documentation of the director’s decision on any requests to reduce the number of spaces;

e.  the requirements and process for income limits and income verification, in accordance with federal, state and county standards;

f.  the specific water and energy conservation measures proposed;

g.  the consequence of any failure to satisfy the requirements of the covenant, which consequences shall include, but not be limited to, specific performance and disgorgement of any revenue that resulted from a rental or sale price that exceed that allowed by the covenant; and

h.  an acknowledgement that King County can enforce the covenant through a judicial action or K.C.C. Title 23; and

2.  Any necessary information identified through the preapplication process.  (Ord. 18623 § 9, 2017).

Ordinance 18623

Ordinance 18623. The plan has since been amended, but no changes to the Overlay have been made since its original adoption in 2017.

Vashon-Maury Island Community Service Area Subarea Plan, page 7

Ibid, page 35

See full text in Appendix A

The adopted deadline to transmit this evaluation to the King County Council was December 31, 2020. In response to COVID-19 the Council approved Motion 15620, extending the due date for any report, study and other work product due in 2020 by sixty days, resulting in a transmittal deadline for this report of March 1, 2021.

Section 9 of Ordinance 18623

The boundary of the Vashon Rural Town is defined in the King County Comprehensive Plan.  The Vashon Rural Town is served with more urban-type utilities and amenities than lands outside of the Rural Town, including more intensive multi-family residential, mixed-use, commercial, and industrial land uses.

See full text in Appendix B

The 2018 AMI for a family of four in King County is $110,321 (King County Housing Authority).  80 percent AMI is $95,250; 60 percent is approximately $71,437.

Development condition VS-P29 limits residential density for mixed use development in the Community Business zone within the Vashon Rural Town to eight units per acre.

K.C.C. Chapter 21.34 - Residential Density Incentives

https://www.huduser.gov/portal/datasets/cp.html

As of the writing of this report, 2018 is the latest year for which HUD Comprehensive Housing Affordability Strategy data was available.

K.C.C. 28.84.050.2

VS-P31: Affordable Housing Development

In their pre-application questions, applicants asked whether the Overlay waives the conditional use permit requirement for exceeding base density.

https://www.kingcounty.gov/depts/community-human-services/housing/affordable-housing-committee.aspx; Ordinance 19119

https://www.kingcounty.gov/depts/local-services/permits/property-research-maps/property-specific-development-conditions/DPA/DPA-Alternative-Housing-Demonstration-Project.aspx

Ordinance 18623