### Attachment B: Bellevue-Redmond – B Line		Revised 12/08/09

CONDITIONS OF APPROVAL: IF the following provisions are not met, the alignment of the B Line between NE 24th Street and NE 31st Street shall be along 156th Avenue NE.  Otherwise, routing shall be consistent with the map included herein.

Condition

The City of Redmond will maintain a pair of bus stops on 152nd Avenue NE for the County in the general area near NE 26th Street to serve the Overlake park-and-ride.  The City of Redmond has agreed to implement Project 29 (conversion of 152nd Avenue NE from four lanes to three lanes) identified in Ordinance 15756, approved by the King County Council and the City Council.  The City of Redmond must finance, design and construct bus bulbs that allow King County Metro to stop in-lane for boardings and alightings on 152nd Avenue NE, and construct a C-Curb or other solid median that prevents other traffic from passing the bus while stopped.  These improvements may be phased as noted in Exhibit 1 of the Transit Speed and Reliability Partnership Agreement between King County, City of Bellevue and City of Redmond.

Bellevue-Redmond Corridor Stop Spacing and Station Locations

Stop Spacing

Stops along the Bellevue-Redmond RapidRide alignment are spaced on average 2,280 feet apart, somewhat less than half a mile (.43 mile).  This includes a segment of Northeast Eighth Street, between the Bellevue Transit Center and Crossroads, where RapidRide will provide the only all-day fixed route service and stops are therefore somewhat closer than the desired one-half mile average stop spacing.

Station Locations

Stations are located at or near the following 13 locations on the Bellevue-Redmond RapidRide alignment.  These station locations may be changed due to specific design limitations.

- 108th Avenue NE at NE Sixth Street (Bellevue Transit Center)

- NE Eighth Street at 124th Avenue NE

- NE Eighth Street at 140th Avenue NE

- 156th Avenue NE at NE Tenth Street (Crossroads)

- 156th Avenue NE at NE 16th Place

- 156th Avenue NE at NE 24th Street

- 152nd Avenue NE at NE 26th Street (if conditions are met)

- 156th Avenue NE at NE 40th Street (Overlake Transit Center)

- NE 40th Street at 148th Avenue NE

- 148th Avenue NE at NE 51st Street

- 148th Avenue NE at NE Old Redmond Road

- 148th Avenue NE at NE 87th Street

- NE 83rd Street at 161st Avenue NE (Redmond Transit Center)

In addition, the Bellevue-Redmond RapidRide will serve approximately 11 intermediate locations along the corridor.

.