| Review of the Woodinville Water District Comprehensive Water System Plan Final March 2019 |
| --- |
| Service Area The Woodinville Water District (District) is a Group A water system serving urban and rural area in central King County. The District is bound by the Cities of Bothell and Kirkland to the west, City of Redmond to the south, unincorporated King County to the west and Snohomish County to the north. In addition, the District shares a boundary with the Cross Valley Water District, Alderwood Water & Wastewater District, and Northshore Utility District. The District's retail service area covers approximately 30 square miles of mostly developed urban land serving the entire City of Woodinville and portions of the cities of Bothell, Kirkland, and Redmond. The District also serves many residents of unincorporated King County and a small number of residents of unincorporated Snohomish County. The District's service area is primarily residential with localized commercial developments, including retail stores, shops, and restaurants. Within the retail service area of the District there is one other Group A public water system and approximately 55 Group B, water systems. The District's Capital Improvement Plan for conveyance and treatment improvements projects expenditures of $103,723,000 over the next twenty-year time-period. Water System The District's distribution system consists of approximately 300 miles of water main ranging in size from 2 to 18 inches in diameter. The water main network is relatively new. The District's system consists of 20 individual pressure zones, eight storage facilities, five booster pump stations, and 46 pressure reducing valves. The District's water supply comes from eight pipeline taps along Seattle's Tolt Pipeline Number 1 and two taps along the Tolt Eastside Supply Line. The District also maintains nine emergency interties and one groundwater well for emergency use. Future supply may include Snohomish River water with partner utilities. The District currently serves 12,872 single-family residences and 280 multi-family units along with irrigation and commercial uses. Population increases are expected to be 0.86 percent annually for households and 1.33 percent for employment. The District analyzed demographic data from the Puget Sound Regional Council and from their historical records to create high, medium, and low scenarios for future planning. Average day water demand in 2015 was 4.07 million gallons a day (mgd). Projected average day demand in 2037 is 5.5 mgd. Average urban residential single-family consumption is 162 gallons per day (gpd) while average rural residential single-family consumption is 221 gpd. Reclaimed Water The Brightwater Treatment Plant located north of the District's retail water service area (RWSA) produces reclaimed water that is wheeled through the District’s RWSA to customers located south of the District's service area boundary. There is a possibility that customers within the District could be served by Brightwater reclaimed water in the future. The District completed the King County Water Reclamation Evaluation as part of the plan. SEPA The District completed a State Environmental Policy Act (SEPA) checklist for the Plan and, as lead agency, issued a determination of nonsignificance for the issuance of the Plan on June 26, 2018. There were no appeals. |
| A review of the specific statutes, rules, codes and policies to the water system plan is as follows: |
|  | A. General water plan, King County Code (KCC) 13.24.010 and 13.28 | Comments/findings |
| (1) | Review is applicable to water utilities distributing or obtaining water in unincorporated King County, and/or utilities that are special purpose district created pursuant to Title 57 Revised Code of Washington (RCW). Is there a need to meet the consistency requirements of RCW 43.20.260? | Yes, the Woodinville Water District's Water System Plan (Plan) is subject to King County Council approval under Title 57 RCW. Yes, The Washington State Department of Health (DOH) also needs to demonstrate consistency for the Plan under RCW 43.20.260. |
| (2) | Consistency with King County Comprehensive Plan (KCCP) and development regulations, and policies including KCC 21A.28.040 development standards, provision of adequate supplies for anticipated growth and development. | Yes, the District's Plan is consistent. |
| (3) | Infrastructure for existing and future service areas based on adopted land use map. | Yes. The District's service area is located in both the urban and rural areas. The District used land use data from King County for the rural area and appropriately used the cities of Bothell, Kirkland, and Redmond adopted land use data for the urban area. |
| (4) | Review proposals for modified or expanded service areas based on compliance with utility's approved plan, and ability to meet duty to serve requirement. | Not applicable. The District's service area is well defined and bounded on three sides by other water utilities. The service area has not changed recently and is not expected to change. |
| (5) | Sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes, the Plan demonstrates an ability to provide service consistent with applicable statutes, codes and regulations. The District obtains its water from Seattle Public Utilities (SPU) through its Tolt River distribution mains. Average day water demand is estimated to be 4.07 mgd. Projected average day demand in 2035 is 5.5 mgd. The District is current with its required water quality monitoring with no recent exceedances of contaminants. |
| (6) | Monitor and review effectiveness of purveyor conservation plans if within area covered by an approved Coordinated Water System Plan (CWSP). | The District is within the East King County CWSP. The District along with Seattle and other water utilities participate in the Saving Water Partnership. The District's water use efficiency plan is organized to conform to the requirements of the Water Use Efficiency Rule. |
|  | B. Consistency requirements: 13.24.060 |  |
| (7) | State and local health requirements. | Yes, water purveyed meets State and local health requirements. |
| (8) | Creation and maintenance of logical service areas. | Yes, the service area is logical. |
| (9) | Elimination or prevention of duplicate facilities. | Yes. The District intends to provide service within its service area by means of direct connection. The District does not foresee any need to provide satellite management services, since direct service is available throughout its service area. The District has entered into agreements with neighboring water utilities and maintains interties with adjacent water utilities. |
| (10) | Promotion of most healthful and reliable services to the public. | Yes. In 2004, the District entered into a new, 60-year wholesale water supply agreement with Seattle. Water purveyed by the District complies with public health standards. Forty-six pipeline projects are recommended to ensure required fire flows and water pressure. |
| (11) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Yes, the District's rates for water service are comparable to the rates charged by similar utilities. The District has adopted a graduated rate structure to encourage efficiency of water use. |
|  | King County Comprehensive Plan and other pertinent county adopted plans and policies. | Yes, there is consistency between the District's Plan and the King County Comprehensive Plan. |
| (12) | Basin-wide or multi-basin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology (Ecology) or Department of Health (DOH). | The District has not been involved in multibasin water plans, although it does take part in SPU initiatives. |
| (13) | Applicable state water quality, water conservation, and waste management standards. | Yes, applicable standards are met. The District receives treated water from SPU which does all the testing. The District does coliform monitoring in keeping with State guidelines. The District's distribution system loss (non-revenue or unaccounted-for water) for 2018 was 3.0 percent and the three-year average is 4.4 percent and meets the statutory goal. |
| (14) | Water Resources Act (RCW 90.54). | The Plan makes no connection between the District's conservation program and the requirements of RCWs 90.54.180 and 90.03.386. |
| (15) | Growth Management Act (GMA) (RCW 36.70A). | The District has a conservation program in place. |
| (16) | Groundwater management plans. | The District has one emergency ground water well and is in the process of updating its Well Head Protection plan. |
| (17) | Federally approved habitat conservation plans and recovery plans under the Endangered Species Act (ESA). | As part of its ESA compliance program, the District operates consistent with best management practices as appropriate to protection of endangered species. |
| (18) | Requirements for salmon recovery under Ch. 77.85 RCW, and other plans, including regional water supply or water resource management plans. | Not discussed in Plan. |
|  | C: Countywide Planning Policies |  |
| (19) | G-4: Adopt comprehensive plans that are consistent with the Countywide Planning Policies as required by the Growth Management Act. | Yes, the District adopted a plan that is consistent with Countywide Planning Policies. |
| (20) | EN-19: Promote energy efficiency, conservation methods and sustainable energy sources to support climate change reduction goals. | Not discussed in Plan. |
| (21) | DP-13: All jurisdictions shall plan to accommodate housing and employment targets. This includes coordinating water, sewer, transportation and other infrastructure plans and investments among agencies, including special purpose districts. | Yes, the District asserts it can accommodate population and employment targets of the cities within its service area. |
| (22) | PF-2: Coordinate among jurisdictions and service providers to provide reliable and cost-effective services to the public. | Yes, the District has coordinated with neighboring service providers with interties for emergency supply. |
| (23) | PF-4: Develop plans for long‐term water provision to support growth and to address the potential impacts of climate change on regional water resources. | Sufficient water supply for growth is available. Climate change is not mentioned; however, the District's source water is from the Seattle system. Seattle has considered climate change and water yield from their source. |
| (24) | PF-7: Plan and locate water systems in the Rural Area that are appropriate for rural uses and densities and do not increase the development potential of the Rural Area. | Yes, the District is planning appropriately for rural serves. |
| (25) | PF-8: Recognize and support agreements with water purveyors in adjacent cities and counties to promote effective conveyance of water supplies and to secure adequate supplies for emergencies. | Yes, the District's supply is regionally coordinated, since it purchases its water from SPU under a long-term contract. The District also has agreements with neighboring water systems with interties and emergency back-up. |
| (26) | PF-9: Implement water conservation and efficiency efforts to protect natural resources, reduce environmental impacts, and support a sustainable long‐term water supply to serve the growing population. | The water conservation and efficiency efforts of the District meet the minimum required by statute. The distribution system loss in 2018 was three percent with a three-year rolling average of 4.4 percent. The distribution system loss is within or meets State standards. |
| (27) | PF-10: Encourage water reuse and reclamation, especially for high‐volume non‐potable water users such as parks, schools, and golf courses. | The District evaluated water reclamation opportunities and found use of reclaimed water is not be viable at this time. The Plan includes the King County Water Reclamation Evaluation form in Appendix N. |
|  | D: King County Comprehensive Plan (KCCP) |  |
| (28) | F-107: With special purpose districts or local service providers, plan for provision of services to rural areas. | Yes, the District is planning appropriately for rural serves. |
| (29) | F-108: King County to work with cities and service providers to establish priority areas for public funding of capital facilities. | Yes, King County will do this. |
| (30) | F-201: All facilities and services should be provided in compliance with provisions and requirements of the Endangered Species Act and the Clean Water Act. | Yes, see Number 17. |
| (31) | F-209: In the Rural Area, services provided by agencies should support a rural level of development and not facilitate urbanization. | Yes, the services by the District will support a rural level of development and not facilitate urbanization. |
| (32) | F-210: capital facility plans and capital improvement programs for services to unincorporated King County are consistent with the KCCP. | Yes, the District's Capital Improvement Plan is consistent with the KCCP. |
| (33) | F-211: King County helps coordinate development of utility facilities with other projects that utilize public rights-of-way and easements, where possible. | Not applicable. |
| (34) | F-221: King County shall initiate a sub-area planning process with any service provider that declares, in its capital facilities plan, an inability to meet service needs within service area. | Not applicable as the District did not identify an inability to meet service needs within its service area. |
| (35) | F-223: If a service deficiency is identified in a service provider's existing service area, King County and the applicable service provider shall remedy the deficiency through a joint planning process addressing capital improvement programs and long-term funding strategies. | Not applicable as the District did not identify an inability to meet service needs within its service area. |
| (36) | F-231: King County supports coordination of regional water supply planning, sales of excess water supplies among municipalities in the region, water quality programs and water conservation, reuse and reclaimed water programs. | The District has interties with neighboring utilities to provide emergency water supply. |
| (37) | F-232: Water utilities that obtain water from, or distribute water in unincorporated King County, and water utilities formed as special purpose districts under Title 57 RCW are required to submit water system plans to the county for review and approval and shall describe in their plans how they intend to meet their duty to provide service within their retail service area. | The District does provide water to unincorporated areas. The District is a special purpose district formed under Title 57 RCW. The District can meet its duty to serve in the designated retail service area. |
| (38) | F-246: King County supports interties that allow the transfer of water resources among water utilities to meet the projected demands for growth where such interties meet the requirements of RCW 90.03.383 and are also consistent with any applicable locally adopted comprehensive plans, regional water supply plans, adopted groundwater management plans, watershed plans, approved Coordinated Water System Plans, Endangered Species Act response requirements and Clean Water Act requirements. | The District has multiple intertie with the neighboring water utilities to provide emergency water supply. |
| (39) | F-249: Utilities with more than one thousand service connections required to submit water system plans for approval to King County shall include an evaluation of reclaimed water use opportunities by completing King County's Water Reclamation Evaluation Checklist. | Yes, the District completed King County's Water Reclamation Evaluation Checklist. |
| (40) | F-251: In its review of water system plans, the UTRC shall consider the criteria provided in K.C.C. 13.24.010, 13.24.060, and 13.24.070, and determine the plan's consistency with the following: a. Applicable provisions of the King County Comprehensive Plan, land use plans, and development regulations adopted under the Growth Management Act; b. Approved or adopted regional water resource plans, such as basin plans, groundwater plans, watershed-based conservation and recovery plans developed under ESA, salmon recovery plans developed under chapter 77.85 RCW, water resource plans developed under chapter 90.54 RCW, watershed plans developed under chapter 90.82 RCW, and a regional water supply plan or water resource management plan; c. The county's Regional Wastewater Services Plan; and d. Other applicable provisions of countywide plans managed by King County, as specified in UTRC guidance or checklists. | The UTRC has reviewed the planning data and the District's operations and has found the Plan is consistent with: a. the King County Comprehensive Plan, land use plans and development regulations; b. to the extent applicable, the basin plans, groundwater plans, watershed-based conservation and recovery plans for the service area; and c. other applicable provisions. |
| (41) | F-252: In reviewing proposals for modified and expanded service area boundaries for municipal water suppliers, the UTRC shall consider, in addition to Policy F-251: a. Compliance by the water system with its water system comprehensive plan, including water conservation elements; b. Whether it can meet its duty to provide service within its service area, as required under chapter 43.20 RCW; and c. Consistency with the service provisions of any applicable Coordinated Water System Plan, as adopted in King County Code Chapter 13.28. | Not applicable as the District is not changing its water service area. |
| (42) | F-253: Consistent with Countywide Planning Policies, public drinking water system surface water reservoirs and their watersheds should be managed primarily for the protection of drinking water, but should allow for multiple uses, including recreation, when such uses do not jeopardize drinking water quality standards. Public watersheds must be managed to protect downstream fish and agriculture resources. | Not applicable as the District does not control any surface water reservoirs or watersheds. |
| (43) | F-254: Groundwater-based public water supplies should be protected by preventing land uses that may adversely affect groundwater quality or quantity to the extent that the supply might be jeopardized. The county shall protect the quality and quantity of groundwater used as water supplies through implementation of Policies E-493 through E-497 where applicable. | Not applicable at this time as the District's source of water is surface water. The District does have an emergency back-up well and is developing a Well Head Protection Program. |