Metropolitan King County Council

#### Regional Water Quality Committee

Staff Report

| Agenda Item No.: | 9 |  | Name: | Beth Mountsier |
| --- | --- | --- | --- | --- |
| Briefing No.: | 2010-B0062 |  | Date: | April 7, 2010 |
| Attending: | Despina Strong, Managing Supervisor, Environmental Programs, Wastewater Treatment Division |

SUBJECT:   A briefing and overview of the Industrial Waste Management Program and anticipated Title 28 revisions.

SUMMARY:

The Industrial Waste Program administers regulations affecting businesses that discharge wastewater into King County's sewerage system.  Regulations are designed to prevent businesses from discharging substances that can degrade the wastewater treatment process, harm workers or facilities, or impact water quality.

Since 1969, the Industrial Waste Program has required many industries to pre-treat wastewater before discharging it into the sewer.  Pretreatment has resulted in a major decline of undesirable metals in wastewater received by King County sewage treatment plants and in the biosolids produced by the plants.

The Industrial Waste Program does more than enforce regulations.  It also helps businesses meet regulations by educating them about pollution prevention, waste reduction, and water reuse. Staff work with both large and small companies to make sure they understand the effect that untreated wastewater can have on the environment.

Federal and state law has changed with regard to industrial waste –  therefore King County has gone through a deliberative process to update Title 28 of the King County Code to be in compliance with federal and state standards.  The proposed amendments to code are anticipated to be transmitted to Council in the next month.  The legislation is more operational rather than policy and is therefore anticipated to be referred to the Government Accountability and Oversight Committee.  However, both the Regional Water Quality Committee and Metropolitan Water Pollution Abatement Advisory Committee are being briefed on the anticipated code changes in advance of transmittal of the legislation for discussion and comment.

Wastewater Treatment Division staff will provide a briefing highlighting the function of the Industrial Waste Management Program and the benefits to the wastewater treatment system and water quality and the anticipated changes to Title 28.

BACKGROUND:

The following information summarizes some of the key components of Industrial Waste Program and the types of discharges that are regulated and require permits and the reasons why.

Pretreatment

Sewage treatment plants are designed to break down and treat biological wastes.  Wastewater pollutants such as heavy metals and oils will not break down in the treatment plant; therefore, certain businesses need to treat their wastewater before discharging to the sewer. The pretreatment system, such as oil/water separation, chemical precipitation, or filtration, will depend on the type and concentration of pollutants in the wastewater. If your wastewater requires pretreatment, you are required to get an approval from the Industrial Waste Program before discharging or connecting to the sewer.

Biosolids

Biosolids is the name for the solids produced by the wastewater treatment process. Biosolids, like the treatment plant effluent, must meet federal quality standards in order to be recycled in a beneficial manner. King County currently reuses its biosolids as a

soil conditioner on wheat, barley, and forest lands throughout the state, including the Mountains-to-Sound Greenway Project along I-90. Locally composted biosolids are mixed with sawdust under the GroCo trade name and are available for landscape contractors and homeowners.

Discharge Approvals

The Industrial Waste Program issues several types of discharge approvals. These include permits, discharge authorizations, discharge letters, and verbal approvals. The type of approval is determined by the volume discharged, the nature of the business, the characteristics of the wastewater, and the potential risk to the treatment plant.  A permit is required if you discharge more than 25,000 gallons per day or are a federally regulated industry.

At least twice a year King County conducts routine monitoring of companies that have waste discharge permits. These companies are charged an additional fee depending on what pollutants are present in the wastewater and the volume of the discharge. This

fee covers the costs associated with the management of the permit, sampling, and analysis of the wastewater. These charges are in addition to the base sewer rate charged by the local sewer agency and are billed monthly as part of your sewer bill.

What is the surcharge program?

The Surcharge Program charges industrial or commercial facilities that discharge wastewater having Total Suspended Solids (TSS) in excess of 400 milligrams per liter (mg/L) (equivalent to parts per million or ppm) or a Biological Oxygen Demand (BOD) greater than 300 mg/L. These facilities are charged an additional fee to pay for the costs of treating this high-strength wastewater. There are no limits for TSS or BOD unless you plan to discharge quantities that might adversely affect the sewage treatment facility,

but these facilities are subject to all other discharge limits. The surcharge or high-strength fee is based on the volume of water discharged and the amount of TSS and BOD in the wastewater.  King County monitors the waste strength on a regular basis.

Industries that are typically subject to surcharge fees include:

Bakeries Food processing

Breweries and Wineries Meat and Fish processing

Chemical toilet waste Soft Drink bottlers

Commercial laundries Tanker truck cleaning

Dairy products

Discharge Limits

King County establishes local limits to ensure that industrial discharges do not damage the county’s treatment plants and the surrounding environment. In addition to local limits, some businesses are subject to federal pretreatment regulations which may be stricter than the local limits.

Federal Pretreatment Limits

The federal government has established discharge limits for specific activities. The following is a partial list of industries considered “categorical dischargers.” These companies require a full permit regardless of wastewater discharge volume.

Aluminum forming 			Metal foundries

Battery manufacturing 		Nonferrous metal manufacturing

Coil coating 				Pesticide manufacturing

Copper forming 			Petroleum refining

Electrical/electronic components 	Pharmaceutical manufacturing

Electroplating 				Circuit board manufacturing

Porcelain enameling 			Iron/steel manufacturing

Pulp/paper mills 			Leather tanning finishing

Wood preserving 			Metal finishing

Inorganic chemical manufacturing 	Centralized waste treatment

King County Local Limits

The following pollutants are subject to local limits. These limits apply to all businesses that discharge industrial wastewater to King County’s sewer system.

Metals and cyanide

Heavy metals in excess of the permitted limits can upset or disable treatment plant operations. Heavy metals either pass through the plant into the final effluent discharged to Puget Sound or accumulate in the biosolids.

Fats, oils, and grease (FOG)

FOG from a petroleum or mineral origin (nonpolar FOG) can harm the biological treatment process. Oil/water separators used to pretreat oily wastewater must be approved before installation.  Plans for separators should be submitted to the local sewer utility or to Industrial Waste for review and approval.

Corrosive substances (pH)

Wastewater with a pH either above or below the permitted level can damage the sewer lines and disrupt treatment plant operations. It can also react with other substances in the sewage to create noxious fumes.

Flammable or explosive materials

Sewer lines have been known to explode, causing severe damage to people and property as a result of explosive or flammable materials entering the sewer. To prevent this hazard, certain pollutants are prohibited from the sewer system. Prohibited pollutants include, but are not limited to: gasoline, kerosene, naphtha, benzene, toluene, xylene, ethers, alcohols, ketones, aldehydes, peroxides, chlorates, perchlorates, bromates, carbides, hydrides, and sulfides and any other substances that King County,

the fire department, EPA, or Washington State recognizes as a hazard to the system. When discharging solutions containing any amounts of flammable or explosive substances, businesses or agencies are to contact the Industrial Waste Program. The type of material, degree of hazard, and amount present will determine whether a discharge approval is granted.

Organic compounds

Organic compounds such as solvents, cleaners, thinners, pesticides, and laboratory chemicals may cause toxic gases and fumes in sewer lines. Discharges of pure organic products and discharges of compounds that may affect worker safety or health

problems are prohibited.

Hydrogen sulfide

Hydrogen sulfide is dangerous to breathe and presents serious odor problems. It also reacts with water to form sulfuric acid which in turn destroys sewer lines. The atmospheric hydrogen sulfide limit is 10 ppm measured at a King County designated

monitoring manhole. The soluble sulfide limits may be established on a case-by-case basis.

Solids and food waste

Solids capable of settling can restrict or block flow in sewer lines. The company discharging the solids is liable for any damages caused by sewage backups. Discharge of materials such as ashes, sand, grass, and gravel that can clog sewage flow is prohibited. All waste must contain less than 7 ml/L of solids capable of settling.  All food waste, including food grinder waste, must be capable of passing through a 1/4-inch sieve.

High temperature

High temperature can cause the release of gases in sewers or disrupt treatment plant operation. The temperature of industrial wastewater shall not exceed 65°C (150°F) at the point where the wastewater enters the public sewer system.

ATTACHMENTS:       none