Review of Northeast Sammamish Sewer and Water District’s General Sewer Plan dated September 2022

Service Area The Northeast Sammamish Sewer and Water District’s (District) Service Area includes the northeastern part of the City of Sammamish, generally surrounding the Sahalee Country Club and then down the northern part of the plateau into the Evans Creek drainage in the unincorporated rural area. The current population estimate within the District is approximately 13,400 people; serving nearly 4,673 single-family residences, 58 multi-family residences, and 24 non-residential customers. Much of the District is fully developed and most of the growth is expected to occur along the western ridge of the Sammamish Plateau and the eastern perimeter of the planning area. Even with this additional development potential, the projected population at full build-out is expected to decrease as the projected person per household (pphh) will be lower than the existing pphh. The District’s General Sewer Plan (Plan) projects a total population of 13,310 in the year 2040. It is not expected that the existing commercial connections/number of employees connected within the District will change significantly from the existing numbers consisting of 17 commercial customer connections with 864 full and part-time employees. Sewer System The sewer system encompasses an area of approximately 5.25 square miles with about 4,800 connections serving approximately 15,360 people. The sewer system consists of eight lift stations, 55 miles of sewer main and 1,395 manholes. Wastewater is discharged to the King County interceptor along the King County East Lake Sammamish Trail in Redmond, near the intersection of SR 202 and East Lake Sammamish Parkway, from which it is conveyed to and treated by King County. Capital Improvement Plan (CIP) The District’s CIP includes improvements with a total cost of $4,883,000. The improvements have been developed based on the conclusions reached in the Plan and are prioritized based on those with the most serious deficiencies. Reclaimed Water The Plan did not include an evaluation, as treatment is provided through a King County facility. The Plan does acknowledge there are potential opportunities for application of reclaimed water for irrigation purposes at the local golf course; however, the capital costs of switching from a private water system to reclaimed water source does not appear to be economically feasible. SEPA The District completed a State Environmental Policy Act (SEPA) checklist for the Plan and, as lead agency under SEPA, issued a determination of nonsignificance for the approval of the Plan on December 3, 2021. There were no appeals.

| A review of the specific statutes, rules, codes, and policies to the water system plan is as follows: |
| --- |
|  | A. General and sewer plan-specific requirements of King County Code (KCC) 13.24.010 | Comments/findings |
| (1) | Review and approval by the King County Council is applicable to public or private entities that provide sewer collection or treatment in unincorporated areas of King County as required by KCC ch. 13.24 | The review and approval the Plan is required as the City collects and conveys wastewater to King County’s Interceptors which flow to the King County owned Treatment Plant. The District’s sewer service area extends into unincorporated King County. |
| (2) | The Plan shall be consistent with the King County Comprehensive Plan and development regulations and policies. | The Plan acknowledges the unincorporated King County areas within the service area. The growth projections reflect Puget Sound Regional Council projections. |
| (3) | The Plan shall be adopted by that entity and approved by the King County Council as a prerequisite for the following: Operating in unincorporated King County; Approval of annexation proposals; Granting of new right-of-way franchises and right-of-way franchise renewals; and Approval of right-of-way construction permits, except for emergency permits issued under KCC 14.44.055. | The District adopted the Plan on July 20, 2022 through Resolution No. 4215 prior to submission to the County for approval. The City’s service area extends into unincorporated King County. The District has a franchise agreement with King County (No. 13609) allowing for the construction, operation, and maintenance of a sewer system, which expires August 23, 2024. |
| (4) | Plans should be submitted every six years or sooner if required by the Washington State Department of Ecology (DOE), or whenever sewer conditions have changed significantly within sewer service area. | The District’s last wastewater plan is dated 2011 and was approved by King County through Ordinance 17218 dated November 1, 2011. |
| (5) | Infrastructure for existing and future service areas based on adopted land use map. | Planned land uses were inputs in calculating future saturation flow rates and identification of sewer system improvements. |
| (6) | Sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | The District utilized a hydraulic model with actual flow rate inputs to analyze the sewer system’s ability to convey wastewater flows for the projected growth. |
| (7) | Consistent with Washington Administrative Code (WAC) 173-240-050. | DOE provided comments that address consistency with the WAC and the District provided responses to each comment. DOE approved the Plan on July 11, 2022. |
| (8) | Discuss the following: Existing and planned flows, average and peak; Existing and planned flows for any basin discharging into the County system; Amounts of inflow and infiltration (I/I), in comparison with County standard of 1,100 gallons per-acre-per-day (GPAD) and steps being taken to reduce; Areas of concern regarding corrosion and odor control, and steps being taken to address; and Opportunities for reclaimed water. | The plan includes a discussion of existing and planned flows. The flows referenced in the Plan reflect flows that discharge into the County system. The Plan illustrates that the sewer system’s rate of I/I is significantly less than the County’s standard. The Plan notes that the low I/I rate represents the success of the construction and testing standards which includes PVC pipe sewer construction, raised manhole covers within and solid manhole covers with handholds rather than pick holes. A corrosion and odor problem existed downstream from a lift station force main discharge. The problem was addressed using chemical treatment of the wastewater and manholes downstream of the force main discharge damaged by corrosion. The Plan does acknowledge there are potential opportunities for application of reclaimed water for irrigation purposes at the local golf course; however, the capital costs of switching from a private water system to reclaimed water source does not appear to be economically feasible. |
|  | B. Public Sewer Service: KCC 13.24.035 |  |
| (9) | All developments within Urban Growth Area (UGA) served by sewer unless on-site systems are allowed on an interim basis per KCC 13.24.136. | The Plan acknowledges sewer service is required in urban areas, other than to serve one house on an existing lot. |
| (10) | Required elements of a sewerage general plan, as called for in RCW 36.94.010(3), are included in King County Comprehensive Plan and Technical Appendix. | The Plan has the general location and description of treatment and disposal facilities, trunk and interceptor sewers, pumping stations, monitoring and control facilities, channels, local service areas, and a general description of the collection system to serve the service area. The District’s standards and details for constructing extensions to the sewer system is provided in Appendix D of the Plan document. The Plan contains design criteria, and policies to guide the District’s daily operation and maintenance of the sewer system, as well as the District’s plan for growth and improvements. |
|  | C. Consistency requirements: KCC 13.24.060 |  |
| (11) | State and local health requirements. | The Plan was reviewed by DOE and approved on July 11, 2022. The Utilities Technical Review Committee (UTRC) review process included a representative of Public Health - Seattle & King County. |
| (12) | Elimination or prevention of duplicate facilities and a reduction of number of entities providing sewer service in King County. | The City has entered into several service agreements with neighboring districts. |
| (13) | Promotion of most healthful and reliable services to the public. | The Plan’s Customer Service policies and Capital Improvement Plan (CIP) promote healthful and reliable services to the utility’s customers. |
| (14) | Provision of service at a reasonable cost, and maximization of use of public facilities. | The Plan’s Customer Service policies include provisions addressing Timely and Reasonable Service for single family home connections as well as for developers. |
| (15) | Basin wide or multibasin water plans, sewerage plans, or both when approved by DOE or Washington State Department of Health. | The Plan does not refer to the District’s participation with basin wide or multibasin water plans, or sewerage plans. |
| (16) | Applicable state water quality, water conservation (e.g., RCW 90.48.495), and waste management standards. | Provisions for treatment, discharge, and reuse are not included in the District’s Plan. The King County Service Agreement states that King County will provide all service to the District and is the responsibility of King County to receive all flows. |
| (17) | Growth Management Act (GMA), chapter 36.70A RCW. | The Plan conforms to the GMA. Please refer to policy consistency below. |
| (18) | Groundwater Management Plans. | The Plan makes no reference to Groundwater Management Plans. |
| (19) | Federally-approved habitat conservation plans and recovery plans under Endangered Species Act. | The Plan makes no reference to habitat conservation plans and recovery plans. |
| (20) | Requirements for salmon recovery under RCW 77.85, and other plans, including regional water supply or water resource management plans. | The Plan makes no reference to the salmon recovery efforts within the watershed. |
| (21) | Applicable requirements to evaluate opportunities for the use of reclaimed water under chapter 90.46 RCW. | The Plan does acknowledge there are potential opportunities for application of reclaimed water for irrigation purposes, and identifies a specific golf course. |
| (22) | State Environmental Policy Act documentation. | The District completed a State Environmental Policy Act (SEPA) checklist for the Plan and, as lead agency under SEPA, issued a determination of nonsignificance for the approval of the Plan on December 3, 2021. There were no appeals. |
|  | COUNTYWIDE PLANNING POLICIES |  |
| (23) | FW-4: Support fiscal sustainability for infrastructure and services that serve rural areas. | The District limits sewer service in the rural area in conformance with King County policy. Sewer service is provided to one private and five public schools, together with a commercial area located outside the UGA boundary. |
| (24) | PF-11: Require water reuse and reclamation where feasible. | See #8 above. |
| (25) | DP-3 and PF-3: Coordination of capital facilities and service plans to promote efficient land use and reliable and cost-effective services. | The review by the UTRC and approval by the County Council promotes coordination of capital facilities and service plans. |
| (26) | DP- 14: Adopted infrastructure plans are consistent with adopted growth targets. | The growth projections are consistent with the adopted targets. |
| (27) | DP-49, PF-1 and PF-13: Limit the extension of urban infrastructure improvements through the Rural Area. | The Plan recognizes the King County provisions that limit the extension of sewer in the rural area. |
| (28) | PF-12: With few exceptions, require development within the UGA to be served by public sewer. | See #9 above. |
|  | KING COUNTY COMPREHENSIVE PLAN POLICIES |  |
| (29) | F-101 and F04: Forging partnerships in identifying appropriate service providers and coordinate planning efforts. | The review and adoption of the Plan demonstrates partnership and coordination efforts. The District has entered into various agreements with neighboring service providers. |
| (30) | F-107 and F-209: Plan for provision of services to rural areas. | The Plan acknowledges King County provisions addressing sewer service within the rural area and states that future sewer service outside of the UGA must conform to the appropriate King County Comprehensive Plan policies and code provisions. |
| (31) | F-201 and F-210: Water and sewer utilities that provide services to unincorporated King County shall prepare capital facility plans consistent with requirements of the GMA and King County Comprehensive Plan. | The Plan is consistent with the GMA and King County Comprehensive Plan as it limits service to areas outside of the UGA and incorporates future growth projections consistent with King County’s adopted growth targets. |
| (32) | F-255: All development within UGA to be served by public sewers, with few exceptions. | See #9 above. |
| (33) | F-256: King County and sewer utilities should jointly plan for phasing out of on-site systems within UGA. | The Plan’s Customer Services policies acknowledge if existing on-site septic systems fail, connection may be required per State WAC provisions. |