| Review of the City of North Bend Water System Plan 2020 |
| --- |
| Service Area The City of North Bend’s (City) water system serves the City as well as portions of the surrounding rural communities. The communities are located in the valley between Rattlesnake Ridge to the south and Mount Si to the northeast. The service area abuts the City of Snoqualmie to the northwest and Sallal Water Association (Sallal) on the southeast. The service area of the City encompasses the Alpine Water Association. The current service area is 8.5 square miles and includes approximately 4.5 square miles of service area within the rural area. The service area is the same as specified in the East King County Coordinated Water System Plan (CWSP). The City serves 2,610 water service connections and a population of 6,625 people. The City’s franchise No. 12780 with the County has expired; an adopted water system plan is required to apply for a new franchise. Water Use Efficiency The City obtains its primary water supply from Mount Si Springs and the Centennial Well. The City also maintains emergency interties with the Sallal Water Association. The estimated per capita per day water production has been reduced from 77.2 gallons in 2010 to just 59.2 gallons in 2019. As of 2019, the City’s distribution system leakage (DSL) was 25.9 percent, with a 3-year rolling average of 22.4 percent. Any DSL value over ten percent requires a Water Loss Control Plan. The City was required to implement such a Loss Control Plan in 2010, but failed to meet targets, and DSL actually increased since that time. The City has now enacted a Water Conservation Ordinance and other measures in an attempt to get DSL under control. The Plan contains an ambitious ten-year capital improvement plan with an estimated cost of $13.9 million. The City would prefer to complete capital improvements with revenues collected from rates to the extent possible. The City identified multiple funding sources for the proposed improvement projects: grants, loans, bonds, as well as other sources including local improvement districts, developer extensions, and general facilities charges. Total water revenues for the City in 2020 were projected at $2.6 million and same year operating expenses were also $2.6 million. The City’s operating and capital budgets are heavily reliant on connection charges, which provide almost 20% of gross revenues; this could pose capitalization issues if growth slows down or connections can’t be provided due to lack of water availability. Reclaimed Water and Regional Planning The City has completed the required Reclaimed Water Evaluation Checklist. It currently uses treated wastewater as a mitigation source for its groundwater pumping operations, and therefore doesn’t have any spare reclaimed water for typical non-potable uses (irrigation, industrial processes, etc.) SEPA The City completed a State Environmental Policy Act checklist and subsequently issued a determination of non-significance (DNS) for the issuance of the plan on March 27, 2020; there were no appeals. The City authored an addendum to the DNS, on November 18, 2020, for changes made to the plan between March 2020 and October 2020. |
| A review of the specific statutes, rules, codes and policies to the water system plan is as follows: |
|  | A. General water plan, King County Code (KCC) 13.24.010 and 13.28 | Comments/findings |
| (1) | Review is applicable to water utilities distributing or obtaining water in unincorporated King County, and/or utilities that are special purpose district created pursuant to Title 57 Revised Code of Washington (RCW). Is there a need to meet the consistency requirements of RCW 43.20.260? | Yes, the Washington State Department of Health (DOH) also needs the County to affirm consistency for the Plan under RCW 43.20.260. |
| (2) | Consistency with King County Comprehensive Plan (KCCP) and development regulations, and policies including KCC 21A.28.040 development standards, provision of adequate supplies for anticipated growth and development. | Yes, the City's Plan is consistent with KCCP and County policies. |
| (3) | Infrastructure for existing and future service areas based on adopted land use map. | Yes, the City used King County’s adopted land use maps for service in the unincorporated area. |
| (4) | Review proposals for modified or expanded service areas based on compliance with utility's approved plan, and ability to meet duty to serve requirement. | The City has proposed to annex two large development parcels from the Sallal Water Association service area and has issued Conditional Certificates of Water Availability to provide service. |
| (5) | Sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes, the Plan demonstrates an ability to provide service consistent with applicable statutes, codes, rules and regulations. The City’s water supplies are at risk of non-compliance with Ecology’s water right issued for the Centennial Well if groundwater withdrawals are not properly mitigated. The Plan approval is necessary for the City to obtain other sources of mitigation and potable supply. Given the City’s previous non-compliance with securing mitigation supply, and with failing to secure an intertie agreement with Sallal, and with failing to reduce distribution system loss since 2010, the UTRC recommends a shorter plan approval period (five years instead of the standard ten years), so that compliance can be ascertained sooner than later. |
| (6) | Monitor and review effectiveness of purveyor conservation plans if within area covered by an approved Coordinated Water System Plan (CWSP). | The City is within the East King County Coordinated Water System Plan. The City’s water use efficiency plan identifies conservation activities which the City employs as part of its long-range conservation plan. The City’s conservation measures include customer education, a water shortage plan, a water conservation ordinance, and a conservation rate structure. The City should explore rebate and retrofit programs in the future. |
|  | B. Consistency requirements: 13.24.060 |  |
| (7) | State and local health requirements. | Yes, water purveyed meets State and local health requirements per reporting in the SENTRY system. |
| (8) | Creation and maintenance of logical service areas. | Due to denials of water service by Sallal Water Association, the City has offered to provide service to rejected parcels. This creates a situation where Sallal’s service area will now, in effect, be bisected by the City’s area of new service. The boundaries are not logical, but a necessary consequence. |
| (9) | Elimination or prevention of duplicate facilities. | Where Sallal has not been able to provide service to new customers, the City has offered to provide service. This will result in duplicate but necessary facilities. |
| (10) | Promotion of most healthful and reliable services to the public. | Yes. Water purveyed by the City complies with DOH requirements. The water is chlorinated but not fluoridated. No complaints have been reported in the last five years. |
| (11) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Cost of service is comparable to other water purveyors in the region. |
| (12) | King County Comprehensive Plan and other pertinent county adopted plans and policies. | Yes, there is general consistency between the City's Plan and the KCCP. |
| (13) | Basin-wide or multi-basin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology (Ecology) or Department of Health (DOH). | The City has not been involved in multi-basin water plans. The City has a wastewater utility, which provides treated wastewater as mitigation supply. |
| (14) | Applicable state water quality, water conservation, and waste management standards. | Yes, applicable standards are met. The City does coliform monitoring in keeping with State guidelines. The City's three year rolling average distribution system loss (non-revenue or unaccounted-for water) is 22.4% which greatly exceeds the statutory goal. A Water Loss Control Plan is mandated by state law to reduce the DSL to under ten percent. |
| (15) | Water Resources Act (RCW 90.54). | The City will enact a new Water Loss Control Plan to comply with DOH’s Water Use Efficiency Rule. |
| (16) | Growth Management Act (GMA) (RCW 36.70A). | The bulk of the service area is within the County’s Urban Growth Area but the utility also serves rural area. |
| (17) | Groundwater management plans. | The City obtains all of its source water from groundwater, has developed a Wellhead Protection Program, and has identified the need for a Wellhead Protection Area to protect its water supplies. |
| (18) | Federally approved habitat conservation plans and recovery plans under the Endangered Species Act (ESA). | The City discharges treated effluent as a mitigation measure to maintain in-stream flows in the Snoqualmie River. |
|  | Requirements for salmon recovery under Ch. 77.85 RCW, and other plans, including regional water supply or water resource management plans. | The City discharges treated effluent as a mitigation measure to maintain in-stream flows in the Snoqualmie River; such in-stream flows protect salmonid habitat below Snoqualmie Falls—the falls are an impassable barrier for migrating fish. |
| (19) | C: Countywide Planning Policies |  |
| (20) | G-4: Adopt comprehensive plans that are consistent with the Countywide Planning Policies as required by the Growth Management Act. | Yes, the City adopted a plan that is consistent with Countywide Planning Policies. |
| (21) | EN-19: Promote energy efficiency, conservation methods and sustainable energy sources to support climate change reduction goals. | Not discussed in Plan; the City will consider energy efficiency on a project-by-project basis. |
| (22) | DP-13: All jurisdictions shall plan to accommodate housing and employment targets. This includes coordinating water, sewer, transportation and other infrastructure plans and investments among agencies, including special purpose districts. | Yes, the City asserts it can accommodate population and employment targets of the cities within its service area—provided it is able to obtain additional mitigation sources. |
| (23) | PF-2: Coordinate among jurisdictions and service providers to provide reliable and cost-effective services to the public. | Yes, the City has an emergency-only intertie with Sallal and provides wholesale service to Alpine. |
| (24) | PF-4: Develop plans for long‐term water provision to support growth and to address the potential impacts of climate change on regional water resources. | The City’s plan includes various studies that look at long-term supply issues and is thus attempting to broaden its portfolio of mitigation and supply sources. |
| (25) | PF-7: Plan and locate water systems in the Rural Area that are appropriate for rural uses and densities and do not increase the development potential of the Rural Area. | The City’s service area includes the rural area beyond the UGA boundary; the lack of sewer service in the rural area will prevent further urban-density growth. |
| (26) | PF-8: Recognize and support agreements with water purveyors in adjacent cities and counties to promote effective conveyance of water supplies and to secure adequate supplies for emergencies. | The City has been negotiating with the adjacent Sallal Water Association for thirteen years with no agreement yet reached for integration of their systems. |
| (27) | PF-9: Implement water conservation and efficiency efforts to protect natural resources, reduce environmental impacts, and support a sustainable long‐term water supply to serve the growing population. | The current water conservation and efficiency efforts of the City DO NOT MEET the statutory minimum required by WAC Ch. 246-290. The distribution system loss in 2019 was 25.9 percent with a three-year rolling average of 22.4 percent. The distribution system loss EXCEEDS the State minimum standards of 10% required by WAC Ch. 246-290. The new Plan has a variety of measures to reduce DSL and overall consumption. |
|  | PF-10: Encourage water reuse and reclamation, especially for high‐volume non‐potable water users such as parks, schools, and golf courses. | The Plan does not consider reclaimed water use, as the utility uses 100% of reclaimed water as mitigation supply. |
| (28) | D: King County Comprehensive Plan (KCCP) |  |
| (29) | F-107: With special purpose districts or local service providers, plan for provision of services to rural areas. | The City’s service area includes service within rural area. |
| (30) | F-108: King County to work with cities and service providers to establish priority areas for public funding of capital facilities. | Yes, King County will continue do this. |
| (31) | F-201: All facilities and services should be provided in compliance with provisions and requirements of the Endangered Species Act and the Clean Water Act. | The City’s provision of water service doesn’t rely on impaired waters or habitat; the City meets the Clean Water Act through its compliance with DOH regulations. |
| (32) | F-209: In the Rural Area, services provided by agencies should support a rural level of development and not facilitate urbanization. | The City’s service provision does not increase density in the rural area. |
| (33) | F-210: capital facility plans and capital improvement programs for services to unincorporated King County are consistent with the KCCP. | Yes, the City's Capital Improvement Plan is consistent with the KCCP and future land use. |
| (34) | F-211: King County helps coordinate development of utility facilities with other projects that utilize public rights-of-way and easements, where possible. | The City DOES NOT HAVE an active franchise with the County; the City may apply for one after adoption of this Plan. |
| (35) | F-221: King County shall initiate a sub-area planning process with any service provider that declares, in its capital facilities plan, an inability to meet service needs within service area. | Not applicable as the City did not identify an inability to meet service needs within its service area. |
| (36) | F-223: If a service deficiency is identified in a service provider's existing service area, King County and the applicable service provider shall remedy the deficiency through a joint planning process addressing capital improvement programs and long-term funding strategies. | Not applicable as the City did not identify an inability to meet service needs within its service area. |
| (37) | F-231: King County supports coordination of regional water supply planning, sales of excess water supplies among municipalities in the region, water quality programs and water conservation, reuse and reclaimed water programs. | The City does not currently have any agreements with adjacent purveyors, but as a result of this planning effort, will work with Seattle Public Utilities (SPU), Sallal, City of Snoqualmie, and others to work on regional supply solutions. |
| (38) | F-232: Water utilities that obtain water from, or distribute water in unincorporated King County, and water utilities formed as special purpose districts under Title 57 RCW are required to submit water system plans to the county for review and approval and shall describe in their plans how they intend to meet their duty to provide service within their retail service area. | The City affirms it can meet its duty to serve in the designated retail service area, which includes unincorporated King County. |
| (39) | F-246: King County supports interties that allow the transfer of water resources among water utilities to meet the projected demands for growth where such interties meet the requirements of RCW 90.03.383 and are also consistent with any applicable locally adopted comprehensive plans, regional water supply plans, adopted groundwater management plans, watershed plans, approved Coordinated Water System Plans, Endangered Species Act response requirements and Clean Water Act requirements. | The City has an emergency-only intertie that it constructed with Sallal, but additional negotiation and engineering is required to integrate the systems. The City supplies wholesale water to Alpine Water. The City is exploring regional supply and mitigation solutions with SPU, the City of Snoqualmie, Sallal, and others. |
| (40) | F-249: Utilities with more than one thousand service connections required to submit water system plans for approval to King County shall include an evaluation of reclaimed water use opportunities by completing King County's Water Reclamation Evaluation Checklist. | The City currently uses 100% of its treated effluent as mitigation for its Centennial Well production, therefore none is available for typical reclaimed water uses such as irrigation or industrial processes. |
| (41) | F-251: In its review of water system plans, the UTRC shall consider the criteria provided in K.C.C. 13.24.010, 13.24.060, and 13.24.070, and determine the plan's consistency with the following: a. Applicable provisions of the King County Comprehensive Plan, land use plans, and development regulations adopted under the Growth Management Act; b. Approved or adopted regional water resource plans, such as basin plans, groundwater plans, watershed-based conservation and recovery plans developed under ESA, salmon recovery plans developed under chapter 77.85 RCW, water resource plans developed under chapter 90.54 RCW, watershed plans developed under chapter 90.82 RCW, and a regional water supply plan or water resource management plan; c. The county's Regional Wastewater Services Plan; and d. Other applicable provisions of countywide plans managed by King County, as specified in UTRC guidance or checklists. | The UTRC has reviewed the planning data and the City's operations and has found the Plan is consistent with: a. the KCCP, land use plans and development regulations; b. to the extent applicable, the basin plans, groundwater plans, watershed-based conservation and recovery plans for the service area; and c. other applicable provisions. |
| (42) | F-252: In reviewing proposals for modified and expanded service area boundaries for municipal water suppliers, the UTRC shall consider, in addition to Policy F-251: a. Compliance by the water system with its water system comprehensive plan, including water conservation elements; b. Whether it can meet its duty to provide service within its service area, as required under chapter 43.20 RCW; and c. Consistency with the service provisions of any applicable Coordinated Water System Plan, as adopted in King County Code Chapter 13.28. | The City is expanding its service area to include two large parcels that were denied water service by Sallal. The City’s new plan includes water conservation, water loss control, and a capital plan to minimize future losses. With additional mitigation sources, the City will be able to serve the expanded service area. The City’s proposal is compliant with most of the provisions of the East King County CWSP and of KCC 13.28.055, although the boundaries with Sallal are constantly evolving due to Sallal’s lack of available water. |
| (43) | F-253: Consistent with Countywide Planning Policies, public drinking water system surface water reservoirs and their watersheds should be managed primarily for the protection of drinking water, but should allow for multiple uses, including recreation, when such uses do not jeopardize drinking water quality standards. Public watersheds must be managed to protect downstream fish and agriculture resources. | Not applicable as the City does not control any surface water reservoirs or watersheds. |
| (44) | F-254: Groundwater-based public water supplies should be protected by preventing land uses that may adversely affect groundwater quality or quantity to the extent that the supply might be jeopardized. The county shall protect the quality and quantity of groundwater used as water supplies through implementation of Policies E-493 through E-497 where applicable. | The City has developed a Wellhead Protection Program to protect drinking water sources. A large portion of the City’s Wellhead Protection Area is within unincorporated King County. |