COUNTY ROAD ENGINEER'S	 Project: SE Mount Si ROAD

FIELD NOTES                                          Mount Si BRIDGE #2550A REPLACEMENT

CIP 200994

King County

Department of Transportation

In the matter of the Ordinance of the KING COUNTY COUNCIL for the LOCATION and ESTABLISHMENT of a COUNTY ROAD.  I certify that the field notes and profiles of such survey herewith submitted are correctly prepared and that the map/s herewith transmitted show/s the tracts of land over which said road passes with the names, if known, of the several owners thereof.

_________________________________	__________________

County Road Engineer		              Date

| That the terminal points, general course, and length of said ROAD along the Establishment centerline as described by Reid Middleton Inc. and as surveyed by King County as follows: COMMENCING at the Southeast corner of said Section 10, Township 23 North, Range 8 East, W.M. in King County, Washington; thence South 89°44’21” West along the south line of said Section 10 a distance of 942.97 feet; thence North 49°56’40” East a distance of 15.55 feet to the POINT OF BEGINNING, said point having a calculated NAD83-91 Washington State Plane coordinate of North 178271.93, East 1410777.73 at Engineers Station 55+00; thence continuing North 49°56’40” East a distance of 141.38 feet to Engineers Station 56+41.38 and the beginning of a 656.00 foot radius tangent curve to the left; thence northwesterly along the arc of said curve through a central angle of 16°26’54” an arc length of 188.32 feet to Engineers Station 58+29.70; thence North 33°29’46” East a distance of 333.28 feet to Engineers Station 61+62.98 and the beginning of a 752.00 foot radius tangent curve to the right; thence northeasterly along the arc of said curve through a central angle of 32°30’20” an arc length of 426.63 feet to Engineers Station 65+89.61; thence North 66°00’07” East a distance of 200.98 feet to Engineers Station 68+70.60 and the beginning of a 656.00 foot radius tangent curve to the right; thence southeasterly along the arc of said curve through a central angle of 54°51’58” an arc length of 628.18 feet to Engineers Station 74+98.78; thence South 59°07’56” East a distance of 139.50 feet to Engineers Station 76+38.28, said point being at NAD83-91 Washington State Plane coordinate North 179059.40, East 1412495.84 and the terminus of said description. The length of said Establishment centerline to be 2,138.28 feet or 0.40 miles. |
| --- |
| STATION | DISTANCE FEET | COURSE | CURVE NOTES | REMARKS |
| 55+00 |  |  |  | BEGIN ESTABLISHMENT of the realignment of SE Mount Si Road |
|  | 141.38 | N49(56'40(E |  |  |
| 56+41.38 |  |  | PC curve left R = 656.00' ∆ = 16(26´54( L = 188.32' |  |
| STATION | DISTANCE FEET | COURSE | CURVE NOTES | REMARKS |
| 58+29.70 | 333.28 | N33(29'46(E |  |  |
| 61+62.98 |  |  | PC curve right R = 752.00' ∆ = 32(30´20( L = 426.63' |  |
| 65+89.61 | 200.98 | N66(00'07(E |  |  |
| 68+70.60 |  |  | PC curve right R = 656.00' ∆ = 54(51´58( L = 628.18' |  |
| 74+98.78 | 139.50 | S59(07'56(E |  |  |
| 76+38.28 |  |  |  | END ESTABLISHMENT of the realignment of SE Mount Si Road. |