Review of the King County Water District 54 Comprehensive Water System Plan, February 2011

Service Area King County Water District 54’s (district) service area extends from South 212th Street on the north to the Kent Des Moines Road on the south and from Puget Sound on the west to 14th Avenue on the east. The retail service area is an area of approximately 0.7 square miles and encompasses parts of the City of Des Moines and the City of Normandy Park. The service area is nearly fully developed. As of 2009, the district served a population of approximately 4,817 through an estimated 759 water service connections. The water service connections equate to approximately 1,778 equivalent residential units (ERU). Production of water for ERU averaged 181 gallons per day for the time period 2004 through 2009. ERU production of water averaged 201 gallons per day for the same time period. The service area is surrounded by the Highline Water District service area and is not expected to change in the future. The district does not hold a franchise with the County given there are no unincorporated areas within its service area. Water Use Efficiency The district obtains its water from four groundwater wells. Additionally, the district maintains an emergency intertie with the Highline Water District. With conservation, average per capita water use was 79 gallons per day in 2009 and is projected to be the same in 2030. The average peaking factor is 2.07 which is the ratio of average day demand to peak day demand. A peaking factor of 2.25 is used to project future water use. The annual distribution system loss rate (how much water they lost in distribution) has varied from 10.9 percent to 19 percent in the past few years. The three-year rolling average distribution system loss is 14.1 percent. Given the high distribution system loss, the district is implementing a meter replacement program over the next six years. The Plan contains a six-year capital improvement plan with an estimated cost of approximately $2.41 million. The district identified three funding sources for the proposed improvement projects: developer extensions, rates, and general facility charges. Total water operating revenues for the district in 2010 were estimated to be $801,662 and same year operating expenses were estimated to be $538,450. Reclaimed Water and Regional Planning The district recognizes the value of reclaimed water as a means to conserve and extend the useful life of the potable water supply. The district worked with King County in the development of the regional reclaimed water planning process and has committed to working with its customers and the County as appropriate to assess the feasibility of using reclaimed water for various non-potable water needs. SEPA The district completed a State Environmental Policy Act checklist and delegated lead agency status to the City of Des Moines. The city issued a Determination of Nonsignificance for the issuance of the plan on May 10, 2011; there were no appeals.

| A review of the specific statutes, rules, codes, and policies to the water system plan is as follows: |
| --- |
|  | A. General and water and sewer plan: King County Code (KCC) 13.24.010; 13.28 | Comments/findings |
| (1) | Review is applicable to special purpose districts organized under Title 57 Revised Code of Washington (RCW). Are the consistency requirements of RCW 43.20.260 applicable? | Yes, the district’s 2011 Comprehensive Water System Plan (Plan), is subject to King County Council approval under Title 57 RCW. The Washington State Department of Health (DOH) also needs to determine consistency for the Plan under RCW 43.20.260. The City of Des Moines and City of Normandy Park provided the district a statement of consistency under RCW 43.20.260 that affirmed consistency between their comprehensive plans and the district’s Plan. |
| (2) | Consistency with King County Comprehensive Plan and Development regulations, and policies including KCC 21A.28.040 development standards, provision of adequate supplies for anticipated growth and development. | Yes, the district’s Plan is consistent. |
| (3) | Infrastructure for existing and future service areas based on adopted land use map. | Yes, the district used adopted land use maps. The service area is in the City of Des Moines and City of Normandy Park with no service in unincorporated King County. |
| (4) | Review proposals for modified or expanded service areas based on compliance with utility’s approved plan, and ability to meet duty to serve requirement. | The service area is not expected to change. The district maintains duty to serve policies for its retail service area. |
| (5) | Sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes, the Plan demonstrates an ability to provide service consistent with applicable statutes, codes, rules and regulations. The district obtains its water from groundwater sources. The projected daily demand for 2030 is approximately 0.92 million gallons per day (mgd) without conservation and 0.87 mgd with conservation. With conservation, per capita water use is projected to be 91 gallons per day in 2010 and 88 gallons per day in 2030. The district’s water supplies appear sufficient to meet projected peak day demand in 2030. |
| (6) | Monitor and review effectiveness of purveyor conservation plans if within area covered by an approved Comprehensive Water System Plan (CWSP). | The district is within the South King County CWSP. The district’s water use efficiency plan identifies conservation activities which the district employs as part of its long-range conservation plan. KCC 13.28 relates to the CWSP and conservation goals. The CWSP does not have conservation goals identified after the year 2000; however, the district has continued to incrementally reduce its annual average per-capita consumption. |
|  | B. Consistency requirements: 13.24.060 |  |
| (7) | State and local health requirements. | Yes. |
| (8) | Creation and maintenance of logical service areas. | Yes, the service area is logical. |
| (9) | Elimination or prevention of duplicate facilities. | Yes. The district intends to provide service within its service area by means of direct connection. Satellite management is not being contemplated by the district. The district maintains emergency interties with the Highline Water District and mutual aid agreements with King County Water District 125 and Lakehaven Utility District. |
| (10) | Promotion of most healthful and reliable services to the public. | Yes. Water purveyed by the district complies with DOH requirements. The water is neither chlorinated nor fluoridated. District sampling has shown manganese to be present at levels that presents aesthetic concerns rather than health concerns. The district’s response for manganese will depend on acceptability of the water to customers. The existing combination of water sources provides sufficient capacity to meet the requirements of the district through 2030. |
| (11) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Yes, the district’s rates for water service are comparable to the rates charged by similar utilities. The district has adopted a graduated rate structure to encourage efficiency of water use. |
| (12) | King County Comprehensive Plan and other pertinent county adopted plans and policies. | Yes, there is consistency between the district’s Plan and the King County Comprehensive Plan. |
| (13) | Basin-wide or multibasin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology (Ecology) or DOH. | The district has not been involved in multibasin water plans. The district neither collects nor treats wastewater. The Plan is consistent with the South King County CWSP. |
| (14) | Applicable state water quality, water conservation, and waste management standards. | Yes, applicable standards are met. The district’s 3-year rolling distribution system loss is equal to 14.1 percent for the years 2007 through 2009. The district will implement a water loss control program to remain in compliance with the code. |
| (15) | Water Resources Act (RCW 90.54). | The district will maintain its existing conservation (efficiency) program while complying with DOH’s Water Use Efficiency Rule. |
| (16) | Growth Management Act (GMA) (RCW 36.70A). | The district received consistency statements from the Cities of Des Moines and Normandy Park affirming that the district used planning assumptions and data consistent with adopted cities policies. |
| (17) | Groundwater management plans. | The district owns four groundwater wells. Wellhead protection areas for sources have been developed. |

| (18) | Federally approved habitat conservation plans and recovery plans under the Endangered Species Act (ESA). | No mention of this in the Plan. |
| --- | --- | --- |
| (19) | Requirements for salmon recovery under Ch. 77.85 RCW, and other plans, including regional water supply or water resource management plans. | No mention of this in the Plan. |
| (20) | Applicable requirements to evaluate opportunities for the use of reclaimed water under chapter 90.46 RCW and CO-7. | The Plan discusses briefly the use of reclaimed water, and recognizes the value of reclaimed water as a measure to conserve and extend the useful life of the potable water supply. The district participated with the County in its development of a regional reclaimed water plan and provided information similar to what would have been provided on the King County Reclaimed Water checklist. |
|  | C. King County Comprehensive Plan—consistency with provisions and specific policies (Water System Plan) |  |
|  | COUNTYWIDE PLANNING POLICIES |  |
| (21) | FW-5: management of resources for multiple beneficial uses, including flood and erosion hazard reduction. | Not applicable. |
| (22) | FW-12(c): ensure sufficient water supply for growth and fish habitat needs through long-term planning. | Not applicable. |
| (23) | CA-5, CA-6, and E-434 and policies to protect quantity and quality of groundwater. | The district uses groundwater. The well head protection program is current. |
| (24) | CO-5: water supply shall be regionally coordinated. | Yes; generally. The district is self-supplied and works with the neighboring utilities. The district’s Plan is subject to, and consistent with, the South King County CWSP. |

| (25) | CO-6: aggressive conservation efforts shall be implemented. | The district has a conservation program in place which appears to meet minimum state requirements. |
| --- | --- | --- |
|  | KING COUNTY COMPREHENSIVE PLAN POLICIES |  |
| (26) | F-102: King County will provide or manage countywide services, which include wastewater, water resource management, surface water management, flood warning and floodplain management, protection and preservation of natural resource lands. | Not applicable. |
| (27) | F-104: plan for provision of services to rural areas. | The district’s service area is all urban. |
| (28) | F-105: King County to work with cities and service providers to establish priority areas for public funding of capital facilities. | The capital improvement program (CIP) is adequate and appropriately focused with funding sources identified. |
| (29) | F-201: all facilities and services should be provided in compliance with provisions and requirements of the ESA. | Not applicable. |
| (30) | F-202: ensure adequate supply of public facilities to support communities. | Yes, the district has sufficient water supplies and has an arrangement for emergency supply from the Highline Water District. |
| (31) | F-203: King County will work with cities, special purpose districts, and other service providers to define regional and local services and determine appropriate providers. | Yes. |
| (32) | F-208: support rural levels of development and not facilitate urbanization. | The district’s service area does not include any rural area. |
| (33) | F-209 and F-212: capital facility plans and improvement programs for services to unincorporated King County are consistent with the King County Comprehensive Plan. | Not applicable. |
| (34) | F-210: King County helps coordinate development of utility facilities. | Yes, to the extent applicable, King County will do this. |

| (35) | F-215: King County shall initiate a sub-area planning process with any service provider that declares, in its capital facilities plan, an inability to meet service needs within service area. | Not applicable. The district did not identify any inability to meet service needs within its service area. |
| --- | --- | --- |
| (36) | F-217: where an area-wide sewer, water, or transportation deficiency is identified, King County and applicable service providers shall remedy the deficiency through a joint planning process. | No area-wide water deficiency is identified. |
| (37) | F-225: King County supports coordination of regional water supply planning, sales of excess water among municipalities, water quality programs, and water conservation and reuse programs. | The district has agreements with its neighboring utility for sharing of water during an emergency. |
| (38) | F-226: Group A water systems must meet duty to serve requirement within service area as defined under CWSP or by individual water system plans. | Yes, the district is committed to meeting its duty to serve in the retail service area. |
| (39) | F-227-231: provides a hierarchy of water supply providers in unincorporated King County, depending on whether within UGA or rural areas, with preference for providing water from existing suppliers. | The district recognizes its duty to serve within its service area and is committed to providing water to all its customers within its service area by direct connection. The district may consider indirect service within the future service area. |
| (40) | F-237: King County supports the use of interties consistent with planning, and implementation of approved ESA and Clean Water Act response requirements. | The district is self supplied and maintains an emergency interties with Highline Water district. |
| (41) | F-239: King County partners with utilities to encourage best management practices and conservation through such means as developing reclaimed water, aggressive water conservation and reuse measures; support planned land uses with reliable service at minimum cost; encourage reclaimed water use, focused on large water users such as golf courses and cemeteries. | King County is willing to work with the district on these issues, particularly the evaluation of reclaimed water opportunities. |
| (42) | F-240: Utilities Technical Review Committee (UTRC) to consider (a) consistency with land use plans and development regulations; (b) approved or adopted plans for groundwater, ESA, salmon recovery, water resources, watershed planning, regional water supply plan; and (c) the Regional Wastewater Services Plan. | The UTRC did consider the given issues and recommends approval of the Plan. |
| (43) | F-241: in reviewing proposals for modified and expanded service area boundaries, the UTRC must include an evaluation of the utility’s compliance with its comprehensive water system plan, including water conservation elements, and whether it can meet its duty to provide service; no approval of service area where unable to provide service for reasons in RCW 43.20.260. | The district is not planning to change its service area and cannot expand as it is entirely surrounded by the Highline Water District. |
| (44) | F-243: public drinking water system reservoirs and watersheds should be managed primarily to protect drinking water supplies, but allow multiple uses when not jeopardizing water quality; downstream uses including recreation, fish, and agricultural resources. | Not applicable. |
| (45) | F-244: groundwater supplies should be protected by preventing land uses that may adversely affect quantity or quality. | Yes, this is done by the City of Des Moines critical areas ordinance and implementation of the critical aquifer recharge area code. |