| Review of the Soos Creek Water & Sewer District Sewer Comprehensive Plan |
| --- |
| Service Area The Soos Creek Water & Sewer District owns and operates a municipal sewer system that serves approximately 35 square miles in south King County. The District maintains a number of service agreements with neighboring utility districts, cities and King County for the provision of sewer services. The existing land use and zoning within the planning area is designated by seven jurisdictions: King County, City of Auburn, City of Black Diamond, City of Covington, City of Kent, City of Maple Valley and City of Renton. The District’s planning area is bounded by adjacent jurisdictions with which the District has existing service agreements, and the urban growth boundary. The service area is not expected to significantly change in the future. The District serves approximately 92,500 people. The District holds two franchises with the County. Franchise 13583 (expires July 19, 2024), and Franchise 14916 (expires May 24, 2029)) are for sewer facilities. The District affirmed the franchise areas are current. The District’s system consists of approximately 483 miles of gravity sewer, 32 miles of force mains, and 29 lift stations. The District’s wastewater is treated at the Renton treatment facility operated by King County. Wastewater leaves the District at 19 locations with 11 discharge connections to the Cedar River Water & Sewer District, three to the District of Renton, one to the District of Kent, and four directly to King County trunk lines. The Plan contains a capital improvement plan with an estimated cost of $88,938,000 in sewer capital projects for the near and distant future. Of this, approximately $59,941,000 is recommended to be implemented within the next 10 years, with the remaining projects to be implemented after that period. These costs are based on 2012 dollars. The District identified funding sources for the proposed improvement projects which include rates, general facilities charges and bond proceeds. Reclaimed Water The District may continue to work with King County to identify opportunities and explore ownership and management options to produce and deliver reclaimed water. SEPA The District completed a State Environmental Policy Act (SEPA) checklist for the Plan and, as lead agency, issued a determination of non-significance for the issuance of the Plan on February 6, 2013. There were no appeals. |
|  | A. General and sewer plan-specific: King County Code (KCC) 13.24.010 | Comments/findings |
| (1) | The code is applicable to sewer utilities that provide sewer collection or treatment in unincorporated areas of King County and/or are component agencies of the regional wastewater system. | A portion of the District’s service area lies within unincorporated King County. The District is a component agency of the regional conveyance and treatment system and so review and approval of the plan is pursuant to KCC 28.84.050. The District is also subject to Title 57 and approval by the County Council is required by code. |
| (2) | Plans should be submitted every six years or sooner if required by the Washington State Department of Ecology whenever sewer conditions have changed significantly within the sewer service area. | The District’s sewer plan was approved by King County in 2005 by Ordinance 15302. |
| (3) | The Plan must meet criteria in Revised Code of Washington (RCW) chapter 90.48 as well as KCC as follows: (1) compliance with the development program and policies outlined in the King County Comprehensive Plan for sewage facilities; and (2) compliance with the basin-wide water and/or sewerage plan. | Yes. See the following for specifics on the various King County Comprehensive Plan policies applicable to wastewater plans and consistency with other planning processes. |
| (4) | The District’s infrastructure for existing and future service areas based on adopted land use map. | Yes, for that portion of the service area in unincorporated King County the land use and zoning was appropriately used in determining the sewer demand projection. |
| (5) | The Plan contains sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes. The District used a new system hydraulic model to evaluate its collection capacity and concluded that there is adequate capacity to accommodate peak flows and anticipated growth to the year 2030. |
| (6) | The Plan is consistent with Washington Administrative Code (WAC) 173-240-050. | Yes, the District will seek plan approval from the Department of Ecology. |
| (7) | The Plan discusses the following: Existing and planned flows average and peak; Existing and planned flows for any basin discharging into county system; Amounts of inflow and infiltration (I/I), in comparison with county standard of 1,100 gallons per-acre-per-day (gpad), and steps being taken to reduce; Areas of concern regarding corrosion and odor control and steps being taken; Opportunities for reclaimed water; and Additional information required by the Utilities Technical Review Committee (UTRC). | All are discussed in the Plan: 1, 2, & 3. The existing and planned flow of 70 gallons per day per person is reasonable. The District worked with the King County Wastewater Treatment Division on the regional I/I control program. I/I modeling was done at 1,685 gpad for the North basins and 665 gpad for the South basins. The District does have some sewer sub-basins with high I/I and has committed to continue to work with the Wastewater Treatment Division as initial I/I control projects are implemented and monitored for effectiveness. 4. There were no issues identified with either corrosion or odor control. 5. The District supports King County’s planning efforts regarding reclaimed water opportunities. 6. In its review of the Plan, the UTRC asked for additional information, which has been provided by the District either in the final Plan or in direct communication with the UTRC. |
|  | B. Public Sewer Service: 13.24.035 |  |
| (8) | The Plan proposes that all developments within Urban Growth Area served by sewer unless on-site are allowed as temporary per KCC 13.24.136 and 13.08.070. | There are unserved areas within the District’s sewer service area and the District has a program to extend service to those areas. The District anticipates the residential population served to grow from 92,500 people in 2010 to approximately 115,052 by 2030. |
| (9) | Public sewer is provided in rural towns if approved by King County. | There are no rural towns in the District’s sewer service area. |
| (10) | No public sewer service outside Urban Growth Area unless authorized under KCC 13.24.134. | All of the District’s sewer service area is within the Urban Growth Area. Sewer service is consistent with KCC 13.24.035. The District acknowledges that sewer service beyond the Urban Growth Area would be consistent with KCC 13.24.134. |
| (11) | Required elements of sewerage general plan, as called for in RCW 36.94.010(3), are included in King County Comprehensive Plan and Technical Appendix. | Yes, the Plan has the general location and description of treatment and disposal facilities, trunk and interceptor sewers, pumping stations, monitoring and control facilities, local service areas, and preliminary engineering in adequate detail to assure technical feasibility and, to the extent known, the methods of distributing the cost and expense of the system and the economic feasibility of plan implementation. |
|  | C. Consistency requirements: 13.24.060 |  |
| (12) | State and local health requirements. | The Plan has not yet been reviewed and/or approved by the Department of Ecology. The UTRC review process included a representative of Public Health-Seattle and King County. |
| (13) | Elimination or prevention of duplicate facilities. | The District has written agreements with other sewer providers regarding areas to be served in order to avoid overlapping jurisdiction and to ensure efficiency in the use of existing facilities. |
| (14) | Promotion of most healthful and reliable services to the public. | Yes. |
| (15) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Currently the District charges a rate that is in the affordable range. In general, the District collects revenues in excess of expenditures. |
| (16) | Reduction of number of entities providing sewer service in King County. | The District has written agreements with other sewer providers regarding areas to be served in order to avoid overlapping jurisdiction and to ensure efficiency in the use of existing facilities. |
| (17) | Basin wide or multibasin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology or the Washington State Department of Health. | The District is aware of, and supports, the planning done for salmon recovery purposes. The District is part of the regional wastewater system managed by King County. |
| (18) | Applicable state water quality, water conservation (e.g., RCW 90.48.495), and waste management standards. | Yes. As the District implements water conservation programs, there may be a minimal impact on the operation of the sewer system. |
| (19) | Growth Management Act; chapter 36.70A RCW. | Yes, the Plan is consistent with the King County Comprehensive Plan. See specific policies below. |
| (20) | Groundwater Management Plans. | The Plan does reference groundwater protection as one of the goals of the sewer plan. |
| (21) | Federally-approved habitat conservation plans and recovery plans under Endangered Species Act, and other plans, including regional water supply or water resource management plans. | The Plan makes no reference to the salmon recovery efforts within the watershed. There is no applicable regional water supply plan. The District developed an Environmental Protection Plan to improve and protect water quality, habitat, aquifers and other environmental values in areas where the District must construct, operate, maintain or replace a sewer system infrastructure to ensure it operates in an environmentally friendly manner. |
| (22) | Applicable requirements to evaluate opportunities for the use of reclaimed water under chapter 90.46 RCW. | Yes, the District supports King County’s planning efforts. |
| (23) | Sewer facilities allowed crossing rural areas only under certain conditions and only for schools or public health emergencies, under certain conditions. KCC 13.24.132. | The District understands and complies with the code. |
| (24) | State Environmental Policy Act documentation. | Determination of Nonsignificance issued by the District on February 6, 2013 with no appeals. |
|  | COUNTYWIDE PLANNING POLICIES |  |
| (25) | PF‐10: Encourage water reuse and reclamation, especially for high‐volume non‐potable water users such as parks, schools, and golf courses. | The District’s may continue to work with King County to identify opportunities and explore ownership and management options to produce and deliver reclaimed water. |
| (26) | PF‐11: Require all development in the Urban Growth Area to be served by a public sewer System with minor exceptions. | Yes, the District is committed to serving the Urban Growth Area. |
| (27) | PF‐12: Prohibit sewer service in the Rural Area and on Resource Lands except: a) where needed to address specific health and safety problems threatening existing structures; or b) as allowed by Countywide Planning Policy DP‐47; or c) as provided in Appendix 5 (March 31, 2012 School Siting Task Force Report). | Yes, the District’s plan demonstrates that service to the rural area will only be done consistent with King County Code. |
|  | KING COUNTY COMPREHENSIVE PLAN POLICIES |  |
| (28) | F-107: plan for provision of services to rural areas. | The District’s service area abuts the rural area. The District’s plan acknowledges that sewer service to the rural area will be done consistent with the King County Code. |
| (29) | E- 408 King County should carry out conservation planning efforts in close collaboration with other local governments, tribes, state and federal governments, land owners, and other conservation planning stakeholders. | Yes. |
| (30) | E-422: King County’s land use planning, regulatory, and operational functions related to environmental protection, public safety, and equity should be closely coordinated across departments and with other applicable agencies and organizations to achieve an ecosystem-based approach. | Not applicable. |
| (31) | E-434: Habitats for species that have been identified as endangered, threatened, or sensitive by the state or federal government shall not be reduced and should be conserved. | Yes, the District operates the system to protect habitat. |
| (32) | F-108 work with cities and service providers to provide services. | Yes, the District has agreements with neighboring service providers to ensure coordinated service. The District holds two franchises with the County. Franchise 13583 and Franchise 14916 are current. |
| (33) | F-202: ensure adequate supply of public facilities to support communities. | Yes. The District included review and incorporation of information from the most recent King County Comprehensive Plan. |
| (34) | F-204: work with cities, special purpose utilities, and other service providers to define regional and local services and determine appropriate providers. | Yes. The District has written agreements with local governments and special purpose utilities regarding service provision and coordination with other systems. |
| (35) | F-208: funding for growth should support facilities needed within Urban Growth Areas, prioritized and coordinated through capital improvement programs (CIP), to comply with concurrency requirements. | Funding sources are identified to support identified needs, including facilities to serve anticipated population growth under local comprehensive plans. Extension of the sewer system will be primarily by developer extension agreements. |
| (36) | F-209: support rural levels of development and not facilitate urbanization. | Yes. |
| (37) | F-211: coordinate development of utility facilities. | Yes, see 34. |
| (38) | F-212: King County’s CIP demonstrates that projected needs for facilities and services can be met within the Urban Growth Area in compliance with concurrency requirements; where not possible, identify strategies including phasing and financing. | Yes. The District’s CIP identifies facilities and a funding strategy to ensure that it will meet anticipated demands. |
| (39) | F-214: water and sewer utilities that provide their services to unincorporated King County, shall prepare capital facility plans consistent with requirements of the Growth Management Act and King County Code. | Yes. |
| (40) | F-221: King County shall initiate a subarea planning process with any service provider that declares, through their capital facilities plan, an inability to accommodate projected service needs inside their service area. | Not applicable as the District has the ability to accommodate projected service needs in the service area. |
| (41) | F-223: if an area wide sewer, water, or transportation deficiency is identified, King County and applicable service providers shall remedy the deficiency through a joint planning process. | Not applicable. |
| (42) | F-255: in the Urban Growth Area, all new development shall be served by public sewers with minor exceptions. | Yes, the District is prepared to serve the urban area. |
| (43) | F- 256: in the Urban Growth Area, King County and sewer utilities should jointly prioritize the replacement of onsite systems that serve existing development with public sewers, based on the risk of potential failure. King County and sewer utilities should analyze public funding options for such conversion and should prepare conversion plans that will enable quick and cost-effective local response to health and pollution problems that may occur when many on-site systems fail in an area. | Yes, the District has policies in place to ensure and encourage the use of the sanitary sewer system within the urban area. Extension of the sewer system will be primarily by developer extension agreements. The District acknowledges that many existing on-site systems exist within its service area and has policies in place to phase out their use over time. |
| (44) | F-259: sewer facilities such as pump stations, force mains and trunk lines that do not provide connections to the Rural Area may be located in the Rural Area only when they are identified in a King County-approved comprehensive sewage system plan and upon a finding by King County that it is technically necessary in providing service to the Urban Growth Area. | Yes, the District understands and abides by this policy. |
| (45) | F-260: on-site facilities in rural and natural resource areas shall be designed, constructed, and operated as permanent facilities. | Not applicable. |
| (46) | F- 261: King County should monitor failing on-site systems and analyze options which may include connecting to sewerage systems where consistent with the King County Comprehensive Plan. | There is no significant number of failing on-site systems within the District’s service area of unincorporated King County. |
| (47) | F-262: collective on-site systems may only be used in rural and natural resource areas under specified conditions. | Not applicable. |