| Review of the Water System Plan for King County Water District 123 |
| --- |
| Service Area King County Water District 123’s (District) service area is an existing Community Group A water system serving the unincorporated town of Preston in King County, Washington. The town of Preston is located between Issaquah and North Bend in rural King County, Washington. The District services a primarily residential area, and currently serves 84 active connections. There are very few remaining lots which can be built or redeveloped under current zoning, and re-zoning for greater density is considered highly unlikely under the 2016 King County Comprehensive Plan. Projected water system buildout is estimated at a maximum of 119 connections. As of 2019, the District served 76 residential connections and 8 non-residential connections; the water service connections equate to approximately 95.0 equivalent residential units (ERU). Production of water per ERU averaged 179 gallons per day for the time period 2013 through 2017, with a peak of 210.7 GPD in 2017. The District currently holds a franchise agreement with the County to conduct permitted construction activities within County rights-of-way, valid until September 2023; the franchise is being renewed and revised at this time. The Plan contains immediate capital improvements needed for the District. The District proposes to construct a new 158,600 gallon reservoir just outside of their retail service area to replace an aging 80,000 gallon concrete tank, which is having difficulty with maintaining fire flow rates. 3200 feet of new transmission mains will be constructed through King County right-of-way to connect to the existing distribution system. The existing tank and mains will be decommissioned, and access to the tank will be removed to make way for fish passage. Water Use Efficiency The District obtains its water from one groundwater well with a capacity of 200gpm. Additionally, the district maintains an intertie with a well privately-operated by Talking Rain bottled water. The average peaking factor is 2.0 which is the ratio of average day demand to peak day demand. The annual distribution system loss rate (how much water they lost in distribution) averages eight percent. These numbers have dropped from nearly twenty percent due to metering and repair programs. The Plan contains a ten-year capital improvement plan with an estimated cost of approximately $1.25 million. The District will be utilizing a USDA Rural Development loan. Total water operating revenues for the District in 2019 were estimated to be $80,760 and same year operating expenses were estimated to be $11,844. Reclaimed Water and Regional Planning The District recognizes the value of reclaimed water as a means to conserve and extend the useful life of the potable water supply, but there is no source of reclaimed water in the area. In the event that reclaimed water is available, the District will make cross-connections available. SEPA The District completed a State Environmental Policy Act checklist and served as lead agency. The District issued a Determination of Nonsignificance for the issuance of the Plan on December 27, 2019; there were no appeals. |
| A review of the specific statutes, rules, codes and policies to the water system plan is as follows: |
|  | A. General water plan, King County Code (KCC) 13.24.010 and 13.28 | Comments/findings |
| (1) | Review is applicable to water utilities distributing or obtaining water in unincorporated King County, and/or utilities that are special purpose district created pursuant to Title 57 Revised Code of Washington (RCW). Is there a need to meet the consistency requirements of RCW 43.20.260? | Yes, the District's Water System Plan (Plan) is subject to King County Council approval under Title 57 RCW. Yes, The Washington State Department of Health (DOH) also needs to demonstrate consistency for the Plan under RCW 43.20.260. |
| (2) | Consistency with King County Comprehensive Plan (KCCP) and development regulations, and policies including KCC 21A.28.040 development standards, provision of adequate supplies for anticipated growth and development. | Yes, the District's Plan is consistent. |
| (3) | Infrastructure for existing and future service areas based on adopted land use map. | Yes, the District used adopted land use maps. The service area is in unincorporated King County around the unincorporated town of Preston. |
| (4) | Review proposals for modified or expanded service areas based on compliance with utility's approved plan, and ability to meet duty to serve requirement. | Not applicable. The service area has not changed recently and is not expected to change. The district maintains duty to-serve policies for its retail service area. |
| (5) | Sufficient information to demonstrate the ability to provide service consistent with the requirements of all applicable statutes, codes, rules, and regulations. | Yes, the Plan demonstrates an ability to provide service consistent with applicable statutes, codes, rules and regulations. The District obtains its water from groundwater sources. Annual demand is approximately 20,000 gallons per day, and maximum daily demand is 40,000 gallons per day. Water use per residential connection is estimated at 254 gallons per day. The District’s water supplies appear sufficient to meet projected peak day demand in 2039. |
| (6) | Monitor and review effectiveness of purveyor conservation plans if within area covered by an approved Coordinated Water System Plan (CWSP). | The District is within the East King County CWSP. The District’s water use efficiency plan identifies conservation activities which the District employs as part of its long-range conservation plan. KCC 13.28 relates to the CWSP and conservation goals. The District’s conservation measures include customer education, a seasonal rate adjustment, and metering/auditing program. |
|  | B. Consistency requirements: 13.24.060 |  |
| (7) | State and local health requirements. | Yes, water purveyed meets State and local health requirements per reporting in the SENTRY system. |
| (8) | Creation and maintenance of logical service areas. | Yes, the service area boundary is logical. |
| (9) | Elimination or prevention of duplicate facilities. | Yes. The District intends to provide service within its service area by means of direct connection. The District does not foresee any need to provide satellite management services, since direct service is available throughout its service area. |
| (10) | Promotion of most healthful and reliable services to the public. | Yes. Water purveyed by the District complies with DOH requirements. The water is neither chlorinated nor fluoridated. No complaints have been reported in the last five years. A series of tests in early October 2019, however, yielded positive coliform results. |
| (11) | Provision of service at a reasonable cost, and maximization of use of public facilities. | Cost of service is comparable to other water districts in the region. |
| (12) | King County Comprehensive Plan and other pertinent county adopted plans and policies. | Yes, there is consistency between the District's Plan and the King County Comprehensive Plan. |
| (13) | Basin-wide or multi-basin water plans, sewerage plans, or both when approved by the Washington State Department of Ecology (Ecology) or Department of Health (DOH). | The District has not been involved in multibasin water plans. The District neither collects nor treats wastewater. The Plan is consistent with the East King County CWSP. |
| (14) | Applicable state water quality, water conservation, and waste management standards. | Yes, applicable standards are met. The District does coliform monitoring in keeping with State guidelines. The District's distribution system loss (non-revenue or unaccounted-for water) is eight percent which meets the statutory goal. |
| (15) | Water Resources Act (RCW 90.54). | The District will maintain its existing conservation (efficiency) program while complying with DOH’s Water Use Efficiency Rule. |
| (16) | Growth Management Act (GMA) (RCW 36.70A). | The retail service area is expected to grow from 84 connections to 101 connections; at maximum system buildout, there could be 119 connections. |
| (17) | Groundwater management plans. | The district owns/operates one groundwater well. Wellhead protection areas for the source has been developed. |
| (18) | Federally approved habitat conservation plans and recovery plans under the Endangered Species Act (ESA). | The Water District does not have surface water usage or discharge which might affect sensitive species or recovery plans. |
|  | Requirements for salmon recovery under Ch. 77.85 RCW, and other plans, including regional water supply or water resource management plans. | The Water District does not have surface water usage or discharge which might affect sensitive species or recovery plans. |
| (19) | C: Countywide Planning Policies |  |
| (20) | G-4: Adopt comprehensive plans that are consistent with the Countywide Planning Policies as required by the Growth Management Act. | Yes, the District adopted a plan that is consistent with Countywide Planning Policies. |
| (21) | EN-19: Promote energy efficiency, conservation methods and sustainable energy sources to support climate change reduction goals. | Not discussed in Plan. |
| (22) | DP-13: All jurisdictions shall plan to accommodate housing and employment targets. This includes coordinating water, sewer, transportation and other infrastructure plans and investments among agencies, including special purpose districts. | Yes, the District has demonstrated it can accommodate population and growth target of the unincorporated town within its service area. |
| (23) | PF-2: Coordinate among jurisdictions and service providers to provide reliable and cost-effective services to the public. | There are no adjacent purveyors. |
| (24) | PF-4: Develop plans for long‐term water provision to support growth and to address the potential impacts of climate change on regional water resources. | The increased water usage associated with population growth within the district can be met using existing water rights and historic production levels. |
| (25) | PF-7: Plan and locate water systems in the Rural Area that are appropriate for rural uses and densities and do not increase the development potential of the Rural Area. | The District’s service area is within the rural area and does not exceed the current planned land use capacity. |
| (26) | PF-8: Recognize and support agreements with water purveyors in adjacent cities and counties to promote effective conveyance of water supplies and to secure adequate supplies for emergencies. | Yes, the District has an intertie with Talking Rain’s private well and system. There are no other adjacent water districts or purveyors. |
| (27) | PF-9: Implement water conservation and efficiency efforts to protect natural resources, reduce environmental impacts, and support a sustainable long‐term water supply to serve the growing population. | The water conservation and efficiency efforts of the District meet the minimum required by WAC 246-290. The distribution system loss in 2017 was 8% which is within State standards of 10% mandated by WAC 246-290. |
|  | PF-10: Encourage water reuse and reclamation, especially for high‐volume non‐potable water users such as parks, schools, and golf courses. | The Plan does not consider reclaimed water use, as the utility does not have reclaimed water infrastructure or a source. |
| (28) | D: King County Comprehensive Plan (KCCP) |  |
| (29) | F-107: With special purpose districts or local service providers, plan for provision of services to rural areas. | The District’s service area is entirely within the rural area. |
| (30) | F-108: King County to work with cities and service providers to establish priority areas for public funding of capital facilities. | Yes, King County will continue do this. |
| (31) | F-201: All facilities and services should be provided in compliance with provisions and requirements of the Endangered Species Act and the Clean Water Act. | The District’s provision of water service doesn’t rely on impaired waters or habitat; the District meets the Clean Water Act through its compliance with DOH regulations. |
| (32) | F-209: In the Rural Area, services provided by agencies should support a rural level of development and not facilitate urbanization. | The District’s development capacity will remain rural in scale over the planning horizon. |
| (33) | F-210: Capital facility plans and capital improvement programs for services to unincorporated King County are consistent with the KCCP. | Yes, the District's Capital Improvement Plan is consistent with the KCCP and future land use. |
| (34) | F-211: King County helps coordinate development of utility facilities with other projects that utilize public rights-of-way and easements, where possible. | The District has a current franchise agreement with the County; the District is renewing its agreement. |
| (35) | F-221: King County shall initiate a sub-area planning process with any service provider that declares, in its capital facilities plan, an inability to meet service needs within service area. | Not applicable as the District did not identify an inability to meet service needs within its service area. |
| (36) | F-223: If a service deficiency is identified in a service provider's existing service area, King County and the applicable service provider shall remedy the deficiency through a joint planning process addressing capital improvement programs and long-term funding strategies. | Not applicable as the District did not identify an inability to meet service needs within its service area. |
| (37) | F-231: King County supports coordination of regional water supply planning, sales of excess water supplies among municipalities in the region, water quality programs and water conservation, reuse and reclaimed water programs. | The District has an intertie with Talking Rain bottled water company for wholesaling and for emergency provision. |
| (38) | F-232: Water utilities that obtain water from, or distribute water in unincorporated King County, and water utilities formed as special purpose districts under Title 57 RCW are required to submit water system plans to the county for review and approval and shall describe in their plans how they intend to meet their duty to provide service within their retail service area. | The District provides water to unincorporated areas. The District is a special purpose district formed under Title 57 RCW. The District can meet its duty to serve in the designated retail service area. |
| (39) | F-246: King County supports interties that allow the transfer of water resources among water utilities to meet the projected demands for growth where such interties meet the requirements of RCW 90.03.383 and are also consistent with any applicable locally adopted comprehensive plans, regional water supply plans, adopted groundwater management plans, watershed plans, approved Coordinated Water System Plans, Endangered Species Act response requirements and Clean Water Act requirements. | The District has an intertie with a private water bottling company to provide emergency water supply. |
| (40) | F-249: Utilities with more than one thousand service connections required to submit water system plans for approval to King County shall include an evaluation of reclaimed water use opportunities by completing King County's Water Reclamation Evaluation Checklist. | The District’s maximum buildout is 119 connections, far less than the 1,000 threshold. |
| (41) | F-251: In its review of water system plans, the UTRC shall consider the criteria provided in KCC 13.24.010, 13.24.060, and 13.24.070, and determine the plan's consistency with the following: a. Applicable provisions of the King County Comprehensive Plan, land use plans, and development regulations adopted under the Growth Management Act; b. Approved or adopted regional water resource plans, such as basin plans, groundwater plans, watershed-based conservation and recovery plans developed under ESA, salmon recovery plans developed under chapter 77.85 RCW, water resource plans developed under chapter 90.54 RCW, watershed plans developed under chapter 90.82 RCW, and a regional water supply plan or water resource management plan; c. The county's Regional Wastewater Services Plan; and d. Other applicable provisions of countywide plans managed by King County, as specified in UTRC guidance or checklists. | The UTRC has reviewed the planning data and the District's operations and has found the Plan is consistent with: a. the King County Comprehensive Plan, land use plans and development regulations; b. to the extent applicable, the basin plans, groundwater plans, watershed-based conservation and recovery plans for the service area; and c. other applicable provisions. |
| (42) | F-252: In reviewing proposals for modified and expanded service area boundaries for municipal water suppliers, the UTRC shall consider, in addition to Policy F-251: a. Compliance by the water system with its water system comprehensive plan, including water conservation elements; b. Whether it can meet its duty to provide service within its service area, as required under chapter 43.20 RCW; and c. Consistency with the service provisions of any applicable Coordinated Water System Plan, as adopted in KCC Ch. 13.28. | Not applicable as the District is not changing its water service area. |
| (43) | F-253: Consistent with Countywide Planning Policies, public drinking water system surface water reservoirs and their watersheds should be managed primarily for the protection of drinking water, but should allow for multiple uses, including recreation, when such uses do not jeopardize drinking water quality standards. Public watersheds must be managed to protect downstream fish and agriculture resources. | Not applicable as the District does not control any surface water reservoirs or watersheds. |
| (44) | F-254: Groundwater-based public water supplies should be protected by preventing land uses that may adversely affect groundwater quality or quantity to the extent that the supply might be jeopardized. The county shall protect the quality and quantity of groundwater used as water supplies through implementation of Policies E-493 through E-497 where applicable. | The District has a Well Head Protection Program. |